## Slide 1: Software Defined Networking (SDN)
Presented by: Syed Asif Raza Shah
CS542, Fall 2016
Papers Presentation
Papers:
  McKeown, Nick, et al. "OpenFlow: enabling innovation in campus networks."
  ACM SIGCOMM Computer Communication Review 38.2 (2008): 69-74.
  Bosshart, Pat, et al. "P4: Programming protocol-independent packet processors."
  ACM SIGCOMM Computer Communication Review 44.3 (2014): 87-95.

## Slide 2: Outline
Paper #1: "OpenFlow: enabling innovation in campus networks."
  Introduction & Motivation
  OpenFlow Switch
  Using OpenFlow
  Conclusion
Paper #2: "P4: Programming protocol-independent packet processors."
  Introduction & Motivation
  Abstract Forwarding Model
  A Programming Language
  P4 Language Example
  Compiling a P4 Program
  Conclusion
  Discussions & Observations: Paper#1 & Paper#2

## Slide 3: Paper #1: "OpenFlow: enabling innovation in campus networks.”

## Slide 4: Introduction & Motivation
Current network infrastructure: enormous installed base equipments and protocols
Blessing and curse for networking researchers
  Work more relevant
  Impact on network innovations
Reluctance to experiment with production traffic
High barriers for new ideas
No practical way to experiment with new network protocols (new routing protocols, alternative to IP, etc)
New ideas untried and untested
Commonly held belief that network infrastructure has “ossified”
What is the solution?
“Programmable Networks”

## Slide 5: Introduction & Motivation (Cont…)
Few questions are focuses:
  How can we run experiments in our campus networks?
  How network admin comfortable to putting experimental equipments?
  How researchers control portion of network that doesn’t disturb others?
  What functionality needed in network switches to enable experiments?
Commercial equipments provides an open, programmable, virtualized platform: Short-term
  Typically do not provide open software platform
  Narrow external interfaces (i.e. just for packet forwarding)
  Internal flexibility is hidden
Few Open platform solutions exist: but insufficient performance and too expensive:
  Operating system based (Linux distribution, XORP)
  ATCA-based virtualized programmable router
  NetFPGA
  This paper proposed a new switch feature that can help extend programmability:
  The OpenFlow Switch

## Slide 6: The OpenFlow Switch
  Initial four goals:
    High-performance & low implementation cost
    Support broad range of research
    Isolate traffic
    Consistent with vendors’ need for closed platforms
  Exploits common set of function of flow-tables of switches & routers
  The OpenFlow Switch consists of three parts:
    Flow Table: Action associated with flow entry to tell switch how to process the flow
    Secure Channel: connect switch to remote control processor (i.e. controller)
    OpenFlow protocol: provide open standard way for controller to communicate with SW
  Categorized switches:
    Dedicated OpenFlow switches
    OpenFlow-enabled switches

## Slide 7: The OpenFlow Switch (Cont…)
  Dedicated OpenFlow Switch:
    An OpenFlow Switch is dump data-path element & just forwards packets between ports as defined by controller
    An entry in Flow-Table has three fields: 1) Packet header defines flows, 2) Action, 3) Statistics
    First generation dedicated OpenFlow switch “Type 0”; Flow header is 10-tuples
  Open-Flow-enabled switches:
    Commercial switches, routers, & APs enhanced with the OpenFlow feature by adding Flow Table

## Slide 8: Using OpenFlow
  Simple example: Amy-OSPF routing protocol replace OSPF
  Amy testing new protocol in network that used by other users. Two additional properties:
    Property 1: Other users packets should be routed using standard routing protocol
    Property 2: Amy only add flow entries for her traffic or Net admin allowed to control
  Other examples:
    Network Management and Access Control: Define a network-wide policy in the central controller, which is enforced directly by making admission control decisions for each new flow.
    VLAN: Traffic identified as coming from a single user (for example, originating from specific switch ports or MAC addresses) is tagged by the switches (via an action)
    Mobile wireless VOIP clients: A controller is implemented to track the location of clients, re-routing connections — by reprogramming the Flow Tables
    A non-IP Network: Flows could be identified using their Ethernet header
    Processing Packets rather than flows: Two ways: 1) In OF-enabled network, default forwarding 2) Route traffic NetFPGA

## Slide 9: Conclusion
  Enables programmability in network
  OpenFlow allow programming for researcher to run experiments on heterogeneous switches & routers in uniform way
  OpenFlow can be implemented in dedicated OF-Switches (“Type 0”) or OF-enabled switches
  Vendors don’t need to expose their internal working
  It can interconnect multiple campus networks easily
  It allow flexibility of network control

## Slide 10: Paper #2: "P4: Programming protocol-independent packet processors."

## Slide 11: Introduction & Motivation
  SDN: Control plane is physically separate from the forwarding plane
  Forwarding devices could be programmed using a common, open, vendor-agnostic interface (like OpenFlow)
  In the Beginning…
    OpenFlow was simple
    A single rule table
      Priority, pattern, actions, counters, timeouts
    Matching on any of 12 fields, e.g.,
      MAC addresses
      IP addresses
      Transport protocol
      Transport port numbers
  Over the Past Five Years…
    Proliferation of header fields
    Multiple stages of heterogeneous tables
    Still not enough (e.g., VXLAN, NVGRE, STT, ...)
Where does it stop?!?

## Slide 12: Introduction & Motivation (Cont…)
  This paper presented concept of future SDN Switches
    Support flexible mechanisms for parsing packets
    Configurable packet parser
      Not tied to a specific header format
    Flexible match+action tables
      Multiple tables (in series and/or parallel)
      Able to match on all defined fields
    General packet-processing primitives
      Copy, add, remove, and modify
      For both header fields and meta-data
  How?
    New generation of switch ASICs
      Chip designs demonstrate flexibility to achieve in custom ASICs at terabit speeds
      But, programming these chips is hard
        Custom, vendor-specific interfaces
        Low-level, akin to microcode programming
    We need a higher-level interface: To tell the switch how we want it to behave

## Slide 13: Introduction & Motivation (Cont…)
  Three main goals of P4:
    Protocol independence
      Switch should not be tied to specific packet formats
      Controller should be able to specify:
        A packet parser for extracting header fields with particular names and types
        Define a set of typed match+action tables
    Target independence
      Program without knowledge of switch details
      Rely on compiler to configure target switch
    Reconfigurability
      Change parsing and processing in the field
Classical OpenFlow (1.x)
P4: Programming Protocol-Independent Packet Processing
OpenFlow 2.0

## Slide 14: Abstract Forwarding Model
  Three generalizations:
    OF fixed parser; P4 support programmable parser allow new headers to be defined
    OF match+actions stages in series; P4 support parallel or series
    P4 model assumes that actions are composed from protocol-independent primitives
  The forwarding model is controlled by two types of operations: Configure and Populate
    Configure operations program the parser, set the order of match+action stages, and specify the header fields processed by each stage
    Populate operations add (and remove) entries to the match+action tables

## Slide 15: A Programming Language
  Abstract forwarding model to define a language to express how a switch is to be configured and how packets are to be processed
  This paper’s main goal is to propose the P4 programming language
  A packet processing language must allow the programmer to express any serial dependencies between header fields
  Dependencies determine which tables can be executed in parallel
  Dependencies can be identified by analyzing Table Dependency Graphs (TDGs); these graphs describe the field inputs, actions, and control flow between tables.
  Unfortunately TDGs are not readily accessible to most programmers
  P4 is designed to make it easy to translate a P4 program into a TDG

## Slide 16: P4 Concepts
  Headers: A header definition describes the sequence and structure of a series of fields. It includes specification of field widths and constraints on field values.
  Parsers: A parser definition specifies how to identify headers and valid header sequences within packets.
  Tables: Match+action tables are the mechanism for performing packet processing. The P4 program defines the fields on which a table may match and the actions it may execute.
  Actions: P4 supports construction of complex actions from simpler protocol-independent primitives.
  Control Programs: The control program determines the order of match+action tables that are applied to a packet. complex actions are available within match+action tables.

## Slide 17: P4 Language Example
  Simple Motivating Example:
    Data-center routing
      Top-of-rack switches
      Two tiers of core switches
      Source routing by ToR
    Assume end-hosts growing and core L2 tables overflowing, MPLS option can simplify the core
    Hierarchical tag (mTag)
      Pushed by the ToR
      Four one-byte fields
      Two hops up, two down

## Slide 18: P4 Language Example: Header Formats
  Header
    Ordered list of fields
    A field has a name and width

## Slide 19: P4 Language Example: Parser
  State machine traversing the packet
    Extracting field values as it goes

## Slide 20: P4 Language Example: Typed Tables
  Describe each packet-processing stage
    What fields are matched, and in what way
    What action functions are performed
    (Optionally) a hint about max number of rules

## Slide 21: P4 Language Example: Action functions
  Custom actions built from primitives
    Add, remove, copy, set, increment, checksum

## Slide 22: P4 Language Example: Control Flow
  Flow of control from one table to the next
    Collection of functions, conditionals, and tables
  For a ToR switch:
Simple imperative representation

## Slide 23: P4 Compiler
  Parser
    Programmable parser: translate to state machine
    Fixed parser: verify the description is consistent
  Control program
    Target-independent: table graph of dependencies
    Target-dependent: mapping to switch resources
  Rule translation
    Verify that rules agree with the (logical) table types
    Translate the rules to the physical tables

## Slide 24: P4 Compiler: Compiling to Target Switches
  Software switches
    Directly map the table graph to switch tables
    Use data structure for exact/prefix/ternary match
  Hardware switches with RAM and TCAM
    RAM: hash table for tables with exact match
    TCAM: for tables with wildcards in the match
  Switches with parallel tables
    Analyze table graph for possible concurrency
  Applying actions at the end of pipeline
            Instantiate tables that generate meta-data
    Use meta-data to perform actions at the end
  Switches with a few physical tables
            Map multiple logical tables to a physical table
            “Compose” rules from multiple logical tables into “cross product” of rules in physical table

## Slide 25: Conclusion
  OpenFlow 1.x
    Vendor-agnostic API
    But, only for fixed-function switches
  An alternate future
    Protocol independence
    Target independence
    Reconfigurability in the field
  P4 language: a straw-man proposal
    To trigger discussion and debate
    Much, much more work to do!

## Slide 26: Discussions & Observations: Paper#1
Our Observations (Performance, Scalability, Efficiency & Security):
  Scalability: How many flows can the flow table handle? How a centralized controller is fast enough to install new flows on switches? How many network devices a centralized controller dynamically manage? Single-point of Failure?
  Efficiency issues as the resources are shared by the research traffic and production traffic?
  When a router or switch fails, how does the network behaves? How does the controller get informed about the loss of a router?
  This paper also doesn’t consider security. If the rules are not configuring correctly or there exist malicious hosts, parallel traffics may influence each other.
  The header fields defined in this paper are very limited. What if we want to more combination?
  Skills required for OpenFlow configuration in switches and routers? How much complexity will be increases for network administrators?

## Slide 27: Discussions & Observations: Paper#2
Our Observations:
  I think making the compiler is really important part and it can bring many bad results like high latency, overhead of switches and so on.
  I wonder if the P4 language and compiler really will not require version-up like OpenFlow 1.x.
  Compatibility issue?
  Just suggested the direction that’s needed for “flexible parsing, flexible actions, and flexible flow control through flexible tables. Why not we should have to think about a generalized framework?
  The heterogeneous nature of the switch environment also makes it tough to develop one API to suit everyone.
  What is the current status for implementing this in hardware and determining how it stacks up against current OpenFlow switches? Performance? Discourage people from using it.
  What if we create intent-driven approach which can provides generalized and abstracted policy semantics for packet processing instead of programming?
  Instead of hardwired packet processing pipeline in an ASIC, The more flexible choice is a network processor, where one of many cores is assigned to actually run code for a given packet.