## Slide 1: CS 540 Network Architecture
Lecture 12: Future Internet, packet classification
Prof. Younghee Lee

## Slide 2: Future of the Internet?
The Internet
  1st Jan 1983. === Flag day
    ARPAnet switched from NCP to TCP/IP
    About 400 machines need to switch.
  As the Internet get bigger, it get much harder to change : Flag day?
  Maybe we reach to almost the summit of the networking system based on the paradigm of the Internet which are “distributed control, stateless,….”
Evolution?
  New requirements: mobility, security, NM, content dissemination…
  Small improvement, higher cost, complexity…
Future of the Internet?:
  Optimistic view: many new challenges for disruptive technologies
  Pessimistic view: networking research is at the end
  Realistic? View: continuous evolution and change
We’re here
The Internet paradigm
Future Network?

## Slide 3: IP evolvability [Kurose]
difficulty: extending existing infrastructure
  investment in legacy systems
  economic incentives?
  works well enough: “if it ain’t broke, don’t fix it”
ossification as a result of success?
approaches towards evolution:
  active (extensible) networks: programmability in net “core”
  overlays: programmability at the “edge”
Straight Jacket
IP convergence!!!
IP
Ossification

## Slide 4: Future of the Internet?
Vision
  Virtual world, virtualization of network
  Connectivity oriented network -> content oriented network
  Service creation by consumer : producer
  Context aware networking: user context, environment context
  Mobile Internet, multi-sensory information
  Virtual real world with emotion [6]
[5]

## Slide 5
Evolutionary or Clean Slate?
Plant the seeds that enable future research experiments*
  Testbed
  Insights from clean slate research help guide the ongoing evolution
Internet as evolving ecosystem*
  Internet monitoring, estimation of traffic flow,
Better network
  Additional value > Transition cost
  Market will decide.
  * Jennifer Rexford, Constatine Dovrolis “Future Internet Architecture: Clean-Slate Versus Evolutionary Research” Communications of the ACM Sep. 2010
  =================================================================================
  Additional value > Transition cost: How?
    Need intelligent & composable open architecture
    Smart network, Smart node: “fit for purposes”

## Slide 6: Smart Network
WDM-PON, OFDM
FTTH
1~10Gbps
Enterprise Network
4G/5G
Backbone
Smart Network
Network Virtualization
: Smart node
: PTN
wired
Super WiFi
wireless
Semantic Web
Linked open Data
Application platform
Web 3.0
Ecosystem
Legacy Internet service, IMS
Smart Network
services
Cloud
Server
Future Internet
Smart Network app. platform

## Slide 7: Internet Plan for future in Korea
Korea Communications Commission (KCC)
  National Agenda for future of the Internet :
    Long term big national initiative
    Future Internet Promotion Committee : 2010.6 ~
Internet Plan for future:
  Report to President of Republic of Korea at 29th June 2011

## Slide 8
Future Network Infra
- Wireless Network
- Optical network
Promotion plan for
New Internet Industry
- Cloud, Contents
- Internet Startup Company
Infra
Key Technology
Security
Globalization
Future Internet R&D
Global R&D Collaboration
Secure Internet
Internet Culture
Vision & Strategy
Total Investment
Government $500M, Private sector $37B for 5 years
<PPP>
Notes: 순서대로 숫자

## Slide 9
Future Network Infrastructure
Network Infra structure for Video and High volume contents oriented Internet service: ’20
Network Infra
Frequency band
4G Service
- LTE : Seoul ’11 ⇒ Nationwide ’14
- WiBro
Gigabit Internet: ’12
⇒ 10Gbps: ’20
Available bandwidth :
- Two times more
100 times faster Internet until 2020
- Investment $7B/year from ISP -
Analog TV : ~ Dec. 2012
Channel(108MHz) , White space
-7-

## Slide 10
Future Internet Technology
Global Testbed
* TEIN : Trans Eurasia Information Network
KOREN
- 10~20Gbps 100Gbps
- Univ./RI open to industry and
public
Mobility, Trustworthy, Content Centric Networking …
Green Internet
Next Generation User Interface, Semantic web
TEIN center: 2012
KOREN
TEIN
Europe
Korea
Future Internet R&D, Global Collaboration
Investment: $250M 2011 ~ 2015

## Slide 11: Internet in Korea: 2010 – report of ITU sep., 2011
Penetration: 97% of household
  Building & Apt. built since 1995
    Broadband Certification System => 36.6% of Fiber connection
  Giga(bit) Internet pilot project
    Includes 100Mbps broadband networks in rural area
Mobile broadband penetration: 91%
Korea tops the ICT Development Index(IDI) by ITU
  ICT diffusion
  ICT use sub-index
  ICT skills sub-index
  ICT network Infra
  .

## Slide 12: Jianli Pan et al., “A Survey of the Research on Future internet architectures”
KEY RESEARCH TOPICS
  Content- or data-oriented paradigms
  Mobility and ubiquitous access to networks
  Cloud-computing-centric architectures
  Security
  Experimental testbeds

## Slide 13
The Third Generation of Networking?
T. Zahariadis et al., “Future Content-Centric Internet Architecture”, FIA 2009
At the beginning:
Overlay Networks of telephone networks
At the beginning:
Overlay Networks of ip networks
Just an example
1891
Mr. Strowger
Overlay Network: network built upon top of underlying network. Connecting nodes with virtual links

## Slide 14: Content- or data-oriented paradigms
Vision
  Find the path to the content (vs. Find the path to the host with ip)
  http://www.datacenterdynamics.com/content-tracks/security-risk/major-ddos-attack-on-dyn-disrupts-aws-twitter-spotify-and-more/97176.fullarticle
CCN or NDN are safer from DDOS attack?

## Slide 15
Van Jacobson et al., “Networking Named Content”, CoNEXT 2009, Rome, Italy
Content traffic in 2008
  500 exabyte (1018)
Networking with Named data
  Rather than named hosts
Content chunk
  simplicity in content routing
    Simplified lower layer (L2)
  Strategy: can select a optimum path according to the situation
  Security: secure content itself (Signature)
    Rather than secure connection
Broadcast
Multiple receivers can receive the content sharing the named data
Content-Centric Network : Van Jacobson

## Slide 16: Mobility and ubiquitous access to networks
Vision
  Mobility as the norm
New Network Architecture
  Scalable, secure,….
  Not evolutionary

## Slide 17: Cloud-computing-centric architectures
Vision
  Virtual world, virtualization of
A major technical challenge
  how to guarantee the trustworthiness of users while maintaining persistent service availability.

## Slide 18: Security
Security was added into the original Internet as an additional overlay instead of an inherent part of the Internet architecture.
  network architecture for security? Not an inherent part of the Internet architecture.

## Slide 19: Experimental testbeds
Developing new Internet architectures requires large-scale testbeds.
Testbed research includes
  multiple testbeds with different virtualization technologies, and the federation and coordination among these testbeds.
United States, EU, Asian countries.

## Slide 20: U.S. projects and clusters on the future Internet.

## Slide 21: Named Data Networking (NDN)
The NDN uses a different model that enables the network to focus on “what” (contents) rather than “where” (addresses).
The data are named instead of their location (IP addresses).

## Slide 22: MobilityFirst
Short term goals:
  Addressing the cellular convergence
  Providing mobile p2p and infostation (DTN) application services.
Long term: V2V and V2I modes
  Location services, georouting, and reliable multicast

## Slide 23: NEBULA
Building a cloud-computing-centric network architecture.

## Slide 24: eXpressive Internet Architecture (XIA)
Directly and explicitly targets the security issue within its design
  Define a rich set of building blocks or communication entities as network principals including hosts, services, contents, and future additional entities.
  It is embedded with intrinsic security by using self-certifying identifiers for all principals for integrity and accountability properties.
  A pervasive “narrow waist” (not limited to the host-based communication as in the current Internet) for all key functions, including access to principals, interaction among stakeholders, and trust management; it aims to provide interoperability at all levels in the system, not just packet forwarding.

## Slide 25: RESEARCH PROJECTS FROM EU

## Slide 26: ICN
Source: ‘A Survey of Information-Centric Networking’ Bengt Ahlgren et al., IEEE Communications Magazine July 2012

## Slide 27: RESEARCH PROJECTS FROM ASIA
JAPAN
CHINA
KOREA

## Slide 28
Packet classification

## Slide 29: Packet classification
Packet classification
  The process of categorizing packets into “flows” in an Internet router
  All packets belonging to the same flow obey a predefined rule and are processed in a similar manner(action) by the router
  Key technology for “open flow” and “SDN”
Flow-aware router: keeps track of flows and perform similar processing on packets in a flow
  Non best effort services, firewalls, QoS
Flow-unaware router (packet-by-packet router): treats each incoming packet individually

## Slide 30: Example of Classification Rules
Access-control in firewalls
  Deny all e-mail traffic from ISP-X to Y
Policy-based routing
  Route IP telephony traffic from X to Y via ATM
Differentiate quality of service
  Ensure that no more than 50 Mbps are injected from ISP-X
Committed Access Rate (rate limiting)
  Rate limit WWW traffic from sub­interface#739 to 10Mbps
Traffic measurement: ftp?, p2p?...

## Slide 31: Multi-field Packet Classification
Given a classifier with N rules, find the action associated with the highest priority rule matching an incoming packet.
Example: packet (5.168.3.32, 152.133.171.71, …, TCP)
 | Field 1 | Field 2 | … | Field k | Action
Rule 1 | 5.3.90/21 | 2.13.8.11/32 | … | UDP | A1
Rule 2 | 5.168.3/24 | 152.133/16 | … | TCP | A2
… | … | … | … | … | …
Rule N | 5.168/16 | 152/8 | … | ANY | AN
Notes: We are given a classifier consisting of n rules. A rule has k fields also called as dimensions, each corresponding to a particular field in the packet header e.g. source and destination IP address or port number or protocol or may be even higher layer fields. Every rule specifies a prefix,a range, a wildcard or any other simple regular expression on each of the k fields. k is the number of dimensions of classification. A rule also has an action associated with it. An incoming packet is said to match a particular rule R, if all fields in the packet’s header match the respective field specifications of rule R. Now a packet may match multiple rules. In that case, the rule with the highest priority is considered. Usually, the order in which rules appear determines their relative priority. As an example a packet …
An example classifier would be access lists in a company firewall where rules determine which packets to allow and which to deny access to the company’s network. In this example actions would be of two types: allow or deny. Another example, that of a 1D classifier, would be destination address forwarding table in a router. Here rules specify prefixes on the destination IP address and actions specify next hops where the matching packets need to be sent to.
Hence packet classification is an important functionality required in routers for differentiated services.

## Slide 32: Complexity: Hard Problem
N rules and k header fields for k > 2
  O(log Nk-1) time and O(N) space
  O(log N) time and O(Nk) space
How many rules?
  Largest for firewalls & similar  1700
  Diffserv/QoS  much larger  100k (?)
    How many actions? : limited number

## Slide 33: Flow-aware Router: Basic Architectural Components
Special processing
Control
Datapath:
per-packet
processing
Routing lookup
Routing, resource reservation, admission control, SLAs
Packet classification
Switching
Scheduling

## Slide 34: Example 4D classifier
Rule | L3-DA | L3-SA | L4-DP | L4-PROT | Action
R1 | 152.163.190.69/255.255.255.255 | 152.163.80.11/255.255.255.255 | * | * | Deny
R2 | 152.168.3/255.255.255 | 152.163.200.157/255.255.255.255 | eq www | udp | Deny
R3 | 152.168.3/255.255.255 | 152.163.200.157/255.255.255.255 | range 20-21 | udp | Permit
R4 | 152.168.3/255.255.255 | 152.163.200.157/255.255.255.255 | eq www | tcp | Deny
R5 | * | * | * | * | Deny
Pkt Hdr | L3-DA | L3-SA | L4-DP | L4-PROT | Rule, Action
P1 | 152.163.190.69 | 152.163.80.11 | www | tcp | R1, Deny
P2 | 152.168.3.21 | 152.163.200.157 | www | udp | R2, Deny
Example Classification Results

## Slide 35: Classification is a Generalization of Lookup
Classifier = routing table
One-dimension (destination address)
Rule = routing table entry
Regular expression = prefix
Action = (next-hop-address, port)
Priority = prefix-length
Longest Prefix Matching for routing lookups is a special-case of one-dimensional packet classification

## Slide 36: Example
Two-dimension space, i.e., classification based on two fields
Complexity depends on the layout, i.e., how many distinct regions are created
Number of region:
n-rule in F dimension
O(nF)

## Slide 37: Classification algorithm
Linear search
  The simplest data structure is a linked list of rules stored in order of decreasing priority
O(N) storage, O(N) lookup time, O(1) update complexity

## Slide 38: Hierarchical Tries
Dimension DA
0
0
0
1
O(NW) memory
O(W2) lookup
Rule | DA | SA
R1 | 0* | 10*
R2 | 0* | 01*
R3 | 0* | 1*
R4 | 00* | 1*
R5 | 00* | 11*
R6 | 10* | 1*
R7 | * | 00*
Search (000,010)
Dimension SA
R5
R2
R1
R3
R6
R7
R4

## Slide 39: Set-pruning Tries [Tsuchiya, Sri98]
Dimension DA
0
0
0
1
Rule | DA | SA
R1 | 0* | 10*
R2 | 0* | 01*
R3 | 0* | 1*
R4 | 00* | 1*
R5 | 00* | 11*
R6 | 10* | 1*
R7 | * | 00*
R7
R2
R1
R5
R7
R2
R1
R3
R7
R6
R7
R4
O(N2) memory
O(2W) lookup
Search (000,010)
Dimension SA

## Slide 40: Grid-of-Tries [Sri98]
Dimension DA
0
0
1
R5
R2
R1
R3
R6
R7
R4
O(NW) memory
O(2W) lookup
0
0
0
0
Rule | DA | SA
R1 | 0* | 10*
R2 | 0* | 01*
R3 | 0* | 1*
R4 | 00* | 1*
R5 | 00* | 11*
R6 | 10* | 1*
R7 | * | 00*
Search (000,010)
0
Dimension SA

## Slide 41: Lookups/Classification with Ternary CAM
TCAM becomes larger, cheaper, and faster as time goes by.
Notes: We have seen that it is quite difficult for a classification algorithm to achieve both speed and modest storage in the worst case. We have found that real classifiers have considerable structure. This makes possible comparatively simple classification schemes which exploit the structure inherent in a classifier. In this talk we saw one such scheme, called RFC which appears to work very well with a selection of classifiers available to us. There fore it seems to be of practical use in applications where classifiers do not change more frequently than a few rules per second on average.
Thanks, that concludes my talk but before we go to questions I would like to appeal to all the members of the audience who work in ISP companies. Researchers working on packet classification need to get access to larger and larger databases of rules. While I understand the business reasons why the ISPs won’t make their policy databases public, I have a set of scripts which would just sanitize them while preserving their structure. So please email me or talk to me if you could help the research community with this. Thanks.

## Slide 42: TCAM: Range-to-prefix explosion
Maximal Prefixes
0011, 01**, 10**
001*, 01**
01**, 10**
01**
0001, 001*, 01**, 10**, 110*, 1110
Rule | Range
R1 | [3,11]
R2 | [2,7]
R3 | [4,11]
R4 | [4,7]
R5 | [1,14]
Maximum memory blowup = factor of (2W-2)d

## Slide 43: Classification with TCAM
The total # of TCAM entries needed to represent a rule is
  Product of the # of TCAM entries needed to represent its range clauses
A rule for two 16 bit field => (2x16 – 2) x (2x16 -2) = 900!
  semantically equivalent rule set that requires less TCAM entries to represent => various approaches
  Multiple Chunks
  . . .
Notes: We have seen that it is quite difficult for a classification algorithm to achieve both speed and modest storage in the worst case. We have found that real classifiers have considerable structure. This makes possible comparatively simple classification schemes which exploit the structure inherent in a classifier. In this talk we saw one such scheme, called RFC which appears to work very well with a selection of classifiers available to us. There fore it seems to be of practical use in applications where classifiers do not change more frequently than a few rules per second on average.
Thanks, that concludes my talk but before we go to questions I would like to appeal to all the members of the audience who work in ISP companies. Researchers working on packet classification need to get access to larger and larger databases of rules. While I understand the business reasons why the ISPs won’t make their policy databases public, I have a set of scripts which would just sanitize them while preserving their structure. So please email me or talk to me if you could help the research community with this. Thanks.

## Slide 44: Recursive Flow Classification [Gupta99]
Difficult to achieve both high classification rate and reasonable storage in the worst case
Real classifiers exhibit structure and redundancy
A practical scheme could exploit this structure and redundancy
Observations:
Notes: We have seen that it is quite difficult for a classification algorithm to achieve both speed and modest storage in the worst case. We have found that real classifiers have considerable structure. This makes possible comparatively simple classification schemes which exploit the structure inherent in a classifier. In this talk we saw one such scheme, called RFC which appears to work very well with a selection of classifiers available to us. There fore it seems to be of practical use in applications where classifiers do not change more frequently than a few rules per second on average.
Thanks, that concludes my talk but before we go to questions I would like to appeal to all the members of the audience who work in ISP companies. Researchers working on packet classification need to get access to larger and larger databases of rules. While I understand the business reasons why the ISPs won’t make their policy databases public, I have a set of scripts which would just sanitize them while preserving their structure. So please email me or talk to me if you could help the research community with this. Thanks.

## Slide 45: RFC: Classifier Dataset
793 classifiers from 101 ISP and enterprise networks with a total of 41505 rules.
  Classifier (policy database)
40 classifiers: more than 100 rules. Biggest classifier had 1733 rules.
Maximum of 4 fields per rule: source IP address, destination IP address, protocol and destination port number.
Notes: Acknowledgments. Say that they are manually entered. And originate largely from acls or firewalls, and hence are updated very infrequently, for example only at router boot time.

## Slide 46: RFC:
Problem formulation:
  Map S bits (i.e., the bits of all the F fields) to T bits (i.e., the class identifier, T= logN, N rules)
Main idea:
  Create a 2S size table with pre-computed values; each entry contains the class identifier
    Only one memory access needed
  …but this is impractical  require huge memory
  Use recursion: trade speed (number of memory accesses) for memory footprint
  3 phases
Notes: Acknowledgments. Say that they are manually entered. And originate largely from acls or firewalls, and hence are updated very infrequently, for example only at router boot time.

## Slide 47: The RFC Algorithm
At each stage the algorithm maps one set of values to a smaller set
  A set of memories return a value shorter than the index of the memory access
Split the F fields in chunks
  1. Use the value of each chunk to index into a table
    Indexing is done in parallel
  2. Combine results from previous phase, and repeat
  3. In the final phase we obtain only one value that is action

## Slide 48: The RFC Algorithm
Source L3 Address
Destination L3 Address
L4 protocol and flags
Source L4 port
Destination L4 port
Type of Service
Packet Header
Chunk #0
Chunk #7
class ID
16bits
16bits

## Slide 49: Deep packet inspection
A form of packet filtering examining the data part of packet and possibly header part
  defined criteria to decide
    whether the packet may pass or
    if it needs to be routed to a different destination, or,
    for the purpose of collecting statistical information.
Applications
  Advanced network management
  Security, viruses, spam, intrusion ; firewall
  internet data mining, eavesdropping, and internet censorship
  ISP(protection from VoIP traffic), Government(national security)
Problem?
  net neutrality
    fear that DPI may be used anti-competitively or to reduce the openness of the Internet

## Slide 50: DPI systems
ASICs
  Requires too much investment
  Hard to upgrade, Applications get locked to a platform
FPGA
  Very flexible but expensive and power-consuming
  Possible to design hybrid H/W and S/W systems
  NetFPGA
Network Processors
  Intel IXP2850
    16 micro-engines with 16 entry CAM, and …
  Cisco QuantumFlow processor
    40 packet processing engines (PPE) each @ 1.2 GHz
Graphics Processors (nVidia)
Issues
  Design algorithms for multiple-core, multi-threaded Commodity processors
  Need to think of hardware-software co-design for high performance DPI engine with high flexibility

## Slide 51: Reading Assignment
Albert Greenberget al., “VL2: A Scalable and Flexible Data Center Network”
Jonathan Perry et al., “Fastpass: A Centralized “Zero-Queue” Datacenter Network”
Monia Ghobadi et al., “ProjecToR: Agile Reconfigurable Data Center Interconnect”
Submit less than 1 page report online via KLMS by 6pm Oct. 31 which is the day before the lecture of Nov. 1st (Tue.)
Submit also hard copy report at the beginning of the lecture of Nov. 1st (Tue.) as attendance check and for discussion