## Slide 1: CS 540 Network Architecture
Lecture 14: TCP for Data Center Networks
Prof. Younghee Lee

## Slide 2
Appropriate TCP for an application
TCP problem
  Just guess what happens in the network or the other end node without any explicit indication from the networks.
    Congestion? Errors? Receiver’s buffer overflow?
    But you can modify TCP for your applications
      You need to understand how TCP works.
      You may either modify TCP or choose appropriate TCP version for your application.
Possible approaches
  Modification of congestion window control mechanism, RTT/RTO, ..
  Congestion control without using packet loss indication
    Proactive control instead of reactive control such as packet loss
  Sending rate control instead of cwnd control
  Use of Explicit Congestion/error indication
  …..

## Slide 3
TCP for Data Center Networks
Transport inside the DC: TCP <= 99.9% of traffic
Partition/Aggregate(query) : delay sensitive
  Incast : n to 1 synchronized mice collide
  Need high burst tolerance
Short messages(coordination, control) : delay sensitive
  Big flows buildup queues: increased latency for short flows
  Need low latency, shallow buffer : AQM –RED?
Large flows(Data update) : Throughput sensitive
  Buffer pressure
  Need high throughput, deep buffer(contradiction): Reduced RTOmin?

## Slide 4
Incast
Incast problem: On Line Data Intensive applications(OLDI)
  Parallel cluster file systems
  Massive multi-server queries
  Web search
  MapReduce: Reduce() procedure
    Small RPC-request/response with tight deadlines
Jacobson’s TCP RTO Estimator
  RTO = SRTT + 4*SDEV
Minimum RTO bound = 200ms
Actual RTO Timer = max(200ms, RTO)
client
switch
servers
Bottleneck
TCP Timeout

## Slide 5
Incast – fine grained RTO
Vasudevan et al. “Safe and effective Fine-grained TCP Retransmissions for Datacenter Communication”, SIGCOMM 2009
  Reduce TCP RTOmin (Unmodified TCP: 200ms): or no RTO Bound
    1 line change in Linux: but1ms timer => not enough
  Use high resolution timers
    Track RTT in microseconds for RTO
    Efficient high resolution kernel timers
    HPET for interrupt signaling
      HPET: High Precision Event Timer: hardware timer

## Slide 6
Incast – fine grained RTO
Still need to improve
Different H/W
Different H/W
Adaptive cwd management?

## Slide 7
Wide area performance without RTOmin
No RTObound (RTOmin) is safe for wide area communications

## Slide 8
Tail latency
Causes
  Device failure, Uneven-split of data btw tasks
  Network congestion for reducers
    Approach: Spread out reducers?: not sufficient
RTT?
  Average RTT: few hundreds of micro sec
  But 5~6% of them : multi msec
  Longest: 10 ~ 20ms
    From Server through multiple intermediate switches => multi hundreds of msec.
    sometimes more than 300 mses => affects OLDI service quality
Approaches
  Make the network faster: HULL, DeTail, DCTCP
    Fat-Tree... + increase throughput: not latency
      but usually smaller tail with faster network
    Eliminate bursts and buffering: Hull(introduce longer latency)
  Optimize how application use the network: Orchestra, CoFlow
  Make the network aware of Dealine: D3, PDQ, D2TCP
    Earlist deadline first: PDQ
    BW reservation for each flow: need extreamly fast control
    Vary sending rate based on both deadline and extent of congestion: D2TCP

## Slide 9
Data Center TCP (DCTCP) SIGCOMM 2010
Explicit Congestion Notification
  Switch: mark packets when queue length exceed threshold k
    F: the fraction of packets that were marked in the last window of data
  Adaptive window decrease
Mark based on instantaneous queue length for faster feedback to better deal with bursts
ECN mechanisms already available in commodity switch.
Exponential moving average

## Slide 10
Data Center TCP (DCTCP)

## Slide 11: Fat Tree Topology [Fares et al., 2008; Clos, 1953]   Multipath TCP: Congestion Control [NSDI, 2011] Map each flow to a path x => use many random paths for a flow => no collision
Multi-Path TCP
K=4
Aggregation Switches
K Pods with
K Switches
each
Racks of
servers

## Slide 12
Multi-Path TCP

## Slide 13
Virtualized Congestion Control from slide of the author
vCC
  Translate between Congestion Control Algorithms in the Hypervisor
  in order to
    Achieve uniform congestion control in multitenant and enterprise datacenters
    Programatically assign congestion control to fine-grained flow signatures
    Simplify rollout of new congestion control algorithms.

## Slide 14
Virtualized Congestion Control http://www.layer9.org/
Q: There are companies that do TCP header modifications. How is this work different from middleboxes?
A: We are proposing several techniques just other than TCP header modifications for congestion control translation.
Q: Could be done outside the server as a middlebox.
A: With middle boxes, you can only to TCP header modifications. You can do more with hypervisors
Q: Is there a cleaner way to do this?
A: Yes, there could be. But, it might not get too complicated if you do this way.

## Slide 15
Virtualized Congestion Control http://www.layer9.org/
Q: Overhead against Open vSwitch (OVS)?
A: We don't use OVS, and we don't have any numbers for OVS yet.
Q: What are the limitations of header modifications. What can't you do?
A: Causing the guests to send if you go more aggressively than normally you would.
Q: What about UDP flows?
A: You might be able to. But requires different techniques.