## Slide 1: CS 540 Network Architecture
Lecture 20 : Named Data Networking
Prof. Younghee Lee

## Slide 2
T. Zahariadis et al., “Future Content-Centric Internet Architecture”, FIA 2009
The third generation of networking
Find the path to destination => Find the path to content/service

## Slide 3
Socio-economic aspect
  Promotion of MM content creation environment, distribution
    Innovative 3D video services
    User generated content
    Shared content
  Interaction between cyber space and real space
Technology aspect
  Video traffic explosion: 40% increase per year
    Video traffic: 80% of future Internet traffic
  Host centric : need to be free from mobility concern
  Security: need to be free from the attack such as DDOS attack
  Current Internet: Overlay Content Network
    <= P2P, Media server, CDN, IPTV, (Smart TV?)
    Scalability problem
    Shortage of bandwidth, large delay
    Pre-planned, application specific,
Why do we need CCN in the Future Internet

## Slide 4
T. Zahariadis et al., “Toward a Content Centric Internet”, IOS press 2010
App for business/entertainment?
Real time Content/Media creation example

## Slide 5
Vinicio Vercellone, “Networking of Information: An information-centric approach to the network of the future”, ETSI Workshop Sophia Antipolis, March 2010
Efficient Internet architecture for Content/media?

## Slide 6
T. Zahariadis et al., “Future Content-Centric Internet Architecture”, FIA 2009
Dissemination Network Node (DNN)
Content distribution: Common dissemination infrastructure for all applications
Augmented Internet – Real-world objects
– Linking real world objects in the virtual information world
Efficient Internet architecture for Content/media?

## Slide 7
Content-Centric Network : Architecture
e2e principle: retains or even expands this design principle
  For robust applications in the face of network failures
Built-in security
  Secured at the network layer
Routing and Forwarding plane separation
  Routing plane can be evolved over time with the best available forwarding technology => research in parallel
Stateful forwarding
  State of recently forwarded packets: caching, loop-detection, flow balance …
Communication driven by receivers (why?)
  Sender need not to manage states

## Slide 8
Van Jacobson et al., “Networking Named Content”, CoNEXT 2009, Rome, Italy
Content traffic in 2008
  500 exabyte (1018)
Networking with Named data
  Rather than named hosts
Content chunk
  simplicity in content routing
    Simplified lower layer (L2)
  Strategy: can select a optimum path according to the situation
  Security: secure content itself (Signature)
    Rather than secure connection
Broadcast
Multiple receivers can receive the content sharing the named data
Content-Centric Network : Van Jacobson

## Slide 9
Van Jacobson et al., “Networking Named Content”, CoNEXT 2009, Rome, Italy
Content-Centric Network : Van Jacobson
FIB: Forwarding table, allows multiple output faces
Content Store: Buffer, also caches Data packets
  (LRU or LFU replacement)
PIT: Pending Interest Table
Processing an Interest:
Matching Data is found in the Content Store => respond with a Data packet and consume Interest
Pending Interest in PIT => add this face to RequestingFaces list
  keeps track of Interests forwarded upstream toward content source(s) so that returned Data can be sent downstream to its requester
Use FIB to forward Interest toward potential source(s) of matching data, add to PIT
Processing data
Data follows a chain if PIT entries back to the source

## Slide 10
Van Jacobson et al., “Networking Named Content”, CoNEXT 2009, Rome, Italy
Content-Centric Network : Van Jacobson
Heirarchical content naming scheme
  Longest match lookup
Transport
  UDP
  CCN Interests that are not satisfied in some reasonable period of time must be retransmitted
  CCN Interests perform the same flow control and sequencing function as TCP ack packets
  receiver’s strategy layer is responsible for retransmission on a particular face (since it knows the timeout for the upstream node(s) on the face) as well as selecting which and how many of the available communication interfaces to use for sending interests

## Slide 11: Securing Content, privacy
CCN trust establishment by associating content namespaces with public keys

## Slide 12: Securing Content, privacy
Content Packet = 〈 name, data, signature 〉
Content
↕ Key
Content
↕ Key
Name Hierarchy & Links
Key Certification Graph
Content
↕ Key
Content
↕ Key
Content
↕ Key
Content
↕ Key
Lack of source addresses in NDN packets provide much better privacy than IP

## Slide 13
Van Jacobson et al., “Networking Named Content”, CoNEXT 2009, Rome, Italy
Content-Centric Network : evaluation

## Slide 14: Distribution from end point communication
ISP
ISP
ISP
ISP
=>
* Some part of this teaching materials are prepared referencing the material presented at IEEE CCW Oct 10, 2011, www.named-data.net
+ Nothing associated with the communication changes with mobility.
Notes: Current Internet architecture is communication- and comm. end-point-centric. But, the nature of the Internet shifted more towards content. Today’s Internet is radio-hostile; mobile-hostile; causes traffic concentration and congestion. It doesn’t deal well with distribution

## Slide 15: Other applications in the works
Audio conferencing
Participatory sensing
Personal data cloud
Media distribution/streaming
VPN server/client
Network monitor/management tools
Pollution sources

## Slide 16: NDN project
One of five on-going projects funded by the U.S. NSF under its Future Internet Architecture Program.: root => CCN
Open question
  Key management
    data authenticity, confidentiality and integrity : everything through key
    Key are themselves named data
    Key management: key distribution, key revocation
  Robust and usable trust management
    that allows content consumers to determine acceptable signing keys in a given context
  Name space design
    Self certifying names, which enable any node to verify that the name in a packet matches its content
  Collaboration with social scientists

## Slide 17: Comparison
Content Centric Networks
  Naming: Hierarchical naming, single address
  Security: Signed content
  Routing: Longest prefix matching
  Caching: Local or network based
  Content existence knowledge: Not part of the CCN core
  Producer-consumer meeting: Propagation of interests
Network of Information (Information centric network) (EU)
  Naming: Flat naming
  Security: Signed content
  Routing: (1) Name resolution (2) Information transfer
  Caching: Network based
  Content existence knowledge: Through name resolution service
  Producer-consumer meeting: Name resolution service provide locations

## Slide 18: Flat name?
No hierarchy: no semantic meaning(just 160bit number)
  No restriction to things for naming
  No DNS-like politics
  Need infrastructure for name resolution service
Not user-friendly in some sense
  Locality
  Performance: overhead,
  Complexity: forwarding
Self-certifying naming
  ID = Hash(Public Key)
  Verify: Ownership without any infrastructure binding ID-> key

## Slide 19: Appendix - early researches -

## Slide 20: New Network Architecture
Current IP
  network location + host identities
Separating them or Data oriented Networking
  ILNPV6, HIP, i3, Layered naming architecture
  ROFL: Route on Flat label
  TRIAD
  DONA
  Content Based Network
  ….

## Slide 21: ROFL: Routing on Flat Labels[2]
Flat host identifiers
  No separate name resolution system required
    DNS
  Simple network configuration, allocation, mobility, multihoming….

## Slide 22: Routing on Flat label?
Scalable routing without aggregation?
  Flat label break aggregation
DHT for scalable routing?
  Assumes point to point routing
  Doesn’t support routing policies
Goal #1: Scale to Internet topologies
  Mechanism: DHT-style routing, maintain source routes to successors/fingers
Goal #2: Support for BGP policies
  Mechanism: Intelligently choose successors/fingers to conform to ISP relationships

## Slide 23: ROFL
Self-certifying identifiers
  Host’s or router’s identity
    Tied to a public-private key pair
    Identifier (ID) : a hash of its public key
Global ring
  Each AS X runs its own ROFL-ring (RR)
  Intradomain, Interdomain

## Slide 24: ROFL
Intradomain
  Joining
    Contacting hosting router
    Chord-like joining algorithm
      Return an ID’s predecessor ID and successor
      Each ID has a source route to its successor and predecessor
  Caching:
  Routing
    Greedy: in the direction of the pointer that is closest
Interdomain
  Cannon-style recursive merging protocol

## Slide 25: ROFL

## Slide 26: ROFL
Policy support in ROFL
Isolation in ROFL (Canon)

## Slide 27: Scalability in ROFL

## Slide 28: ROFL
Performance?
  tolerable
As lookup?
For content routing?
Just an idea?
  Rolling On the Floor Laughing? (ROFL)

## Slide 29: Layered Naming Architecture[1]
DNS: one level of name resolution
Propose: Three levels of name resolution
  from user-level descriptors to service identifiers
  from service identifiers to endpoint identifiers
  from endpoint identifiers to IP addresses
To solve
  Hosts are tied to IP addresses
    Mobility and multi-homing pose problems
  Services are tied to hosts
    A service is more than just one host: replication, migration, composition
  Packets might require processing at intermediaries before reaching destination
    “Middleboxes” (NATs, firewalls, …)

## Slide 30: Layered Naming Architecture
Name Services and Hosts Separately
  Service identifiers (SIDs) are host-independent data names
  End-point identifiers (EIDs) are location-independent host names
  Protocols bind to names, and resolve them
    Apps should use SIDs as data handles
    Transport connections should bind to EIDs

## Slide 31: Naming Layers

## Slide 32: Flat names for SID and EID
Flat names impose no structure on entities
Flat names can be used to name anything
But
Global resolution infrastructure needed
  Perhaps as “managed DHT” infrastructure
Lack of local name control
Lack of locality
Not user-friendly
  User-level descriptors are human-friendly
0xf436f0ab527bac9e8b100afeff394300

## Slide 33: Delegation
Packets might require processing at intermediaries before reaching destination

## Slide 34: TRIAD[5]
The explicit inclusion of a content layer that provides scalable content routing, caching and content transformation
Extensible path-based addressing using this “shim” protocol on top of IPv4
TRIAD: acronym, standing for Translating Relaying Internet Architecture integrating Active Directory

## Slide 35: TRIAD
Conventional Content routing
  DNS or HTTP level redirection
    Name lookup latency limits content transfer times as bw increase
  P2P : proprietary solution
Caching
  Cached data doesn’t reflect current topology

## Slide 36: TRIAD
Content Router
  Perform routing on names as part of a “content layer”
    Perform DNS name request forwarding
    Distribute name reachability information via name-based routing
  Replica sites can be viewed as offering alternate routes to the sane content
user
ContentRouter
Web server
Web server
Web server
Content

## Slide 37: TRIAD
Content Routing Tables
  Forwards requests to peer routers rather than remote servers
    Routing decisions made with local state such as path latency, server latency, and topology
Request Forwarding
  Last-hop CR returns address of server

## Slide 38: TRIAD
Name based Routing
  Content routers exchange advertisements of preferred routes: name, next hop, path, latency
  Servers advertise content, CRs push these advertisements outwards using BGP-like protocol
    BGP with names
Scaling NBR
  Create collections of names as “routing aggregates”

## Slide 39: Data-Oriented Network Architecture (DONA): Problem [11]
Scott Shenker (M. Chowla, T. Koponen, K. Lakshminarayanan, A. Ramachandran, A. Tavakoli, I. Stoica)
Internet was designed for host-to-host communication
  “contact this host...”
Internet is mainly used for data access
  “get me this data.....”
  Mismatch between usage and design:
  data migration and replication unnecessarily hard
  requires Akamai- and BitTorrent-like designs to scale
Question: what would the Internet look like if we designed it around data access?

## Slide 40: Parents of this Work
Failure: ROFL
Mechanisms: HTTP, anycast, pub/sub, SFS, HIP,...
Architecture:
  content routing:TRIAD
  naming: LFN/DOA
no new ideas!

## Slide 41: What Do Users Care About?
Persistence of names:
  Follow data migration
  Today: HTTP redirects, email forwarding
Availability of data: (both latency and reliability)
  Take advantage of replicated data
  Today: Akamai/BitTorrent
Authenticity of data:
  Know that data came from intended source
  Today: securing the channel (IPsec, TLS), or PKI

## Slide 42: Current Barriers
Rigid and Weak Naming: hostname/path
  Ties data to host, making migration/replication hard
  Doesn’t help much with authentication
Protocol Mess: e.g., DNS, TCP, HTTP
  Data isn’t named until the application is invoked
  Caching (and other data handling) is application-specific
  No low-level support for anycast-like service discovery

## Slide 43: Fix #1: Flat, Self-certifying Names
Self-certifying (SFS, HIP)
  Data associated with principal P with public key Kp
  Names are of the form: Hash(Kp): label
  Data requests return: <Kp, label, data, signature>
  Can verify name related to Kp, and Kp signed data
Name not tied to location, so naming isn’t rigid
  resolution mechanism described later

## Slide 44: Fix #2: Better Protocol Structure
Implement replication and caching at lower level:
  find closest replica without application-level tricks
  caching infrastructure not application-specific
DONA does this through two major changes:
  insert data-handling shim layer right above IP
  resolve name by routing to data (TRIAD)
    better fate sharing
    less complicated management
No DNS, no lookup, just routing on names

## Slide 45: Content based Networking
Applications
  Distributed auction systems (e-Bay)
  Information sharing systems (FastTrack, Gnutella)
  Mobile and wireless applications (instant messaging, personalized news distribution)
  Sensor network
New style of communication
  The flow of information – from server to receiver
    is determined by the specific interests of the receiver
    not by explicit destination address of receiver: current IP based network
2016-11-27
45
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
45

## Slide 46: Content based Networking
Multicasting as a Solution?
  Multicast addresses = multicast groups: (unit: group of same interest)
    Sender sends information to reserved address : SAP : announcement
    Receiver “subscribes” for the address
  Problem: How to split information into separate groups to satisfy all users?
    Receiver must subscribe for a most of groups => huge unusable garbage
    A lot of small groups? => sender must send to many groups & receiver must subscribe for many groups
Content based middleware as a solution
  subscription can express predicates over the whole content of publication, not only over few well-known attributes
    Advantage: Greater expressive power
    Disadvantage: Scalability, not distributed but centralized
  (Overlay network)
2016-11-27
46
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
46

## Slide 47: Content based Networking
Still need addresses
  associate predicates with their issuers
  Maintain topological routing info
Predicate advertised by node is implicitly an address
Message set of typed attributes
2016-11-27
47
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
47

## Slide 48: Content based Networking
Routing
  Use advertised predicates to prune branches of broadcast distribution trees
  Router uses 2 protocols
    Broadcast routing
    Content-based routing
      “push” based on recv ads
      “pull” based on snd requests
        To update routing table
        update replies
  Avoids sending out ads that have already been set up
  Use sender requests to collect routing info
2016-11-27
48
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
48

## Slide 49: Content based Networking
Features
  Receivers of message is dynamically determined by the content of message
2016-11-27
49
R
R
R
R
R
R
Message about “movie”
Interest about “movie”
Interest about “movie”
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
49

## Slide 50: Content based Networking
Routing and Forwarding
  Receiver registers its interest (predicate)
  Routers exchange predicates with neighbors periodically
  Advertised predicate is accumulated on each interface
R
I-1(P1)
I-2(P2)
Predicate about “Movie”
Predicate about “Spiderman”
R
Predicate about “Movie”
Predicate about “Diet”
R
Predicate about “Movie” or “Diet”
A sample form of predicate:
[Type = ‘Movie’ Λ Genre = ‘Horror’
Λ Size < 1GB]
A sample form of message:
[Type = ‘Movie’; Title = Spiderman;
Quality = High]
Notes: 50

## Slide 51: Content based Networking
Open issues
  Forwarding algorithm, forwarding table
  Routing (how to update routing table, predicates changes very frequently)
  Reliable Transport Layer
  Security (privacy of receivers’ predicates)
  Benchmarks
2016-11-27
51
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
51

## Slide 52: Formalization of message model
Message consist of attributes
Attribute has
  Type
    Integer
    String
    Boolean
  Name
  Value
Example of datagrams:
  [integer price = 18750, string stock = ‘INTC’]
  [string city=‘Prague’, integer temperature = 25]
2016-11-27
52
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
52

## Slide 53: Formalization of Predicate Model
Constraints on attributes
  Integer
    =, (≠), <, (≤), >, (≥)
  String
    Equality, (inequality), substring, prefix, suffix, <, (≤), >, (≥)
  Boolean
    =, (≠)
Filter = conjunction of constraints = predicate of the every receiver
Example of filter:
  [integer price < 50 ∧ string stock = ‘MSFT’]
  [alert-type=“intrusion” Λ severity>2 V class=“alert” Λ device-type=“web-server”]
2016-11-27
53
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
53

## Slide 54: Forwarding in the CB-Network’s Router
2016-11-27
54
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
54

## Slide 55: Example of Forwarding Table
2016-11-27
55
Forwarding table one-to-one
association of predicates to
Interfaces
Filter
* conjunction of Constraints
* fs,t filter in disjunction of filters for
particular I
Is
* an interface
=> disjunction of Filters
Constraints in 3rd column
- Use counting algorithm to
determine which interface
predicate matches
Notes: Content based networking is an emerging routing paradigm in that:
Message does not have explicit destination address, instead, content of message determines the destination implicitly.
55

## Slide 56: References
Hari Balakrishnan et al., “A Layered Naming Architecture for the Internet”, ACM SIGCOMM, Aug 2004
Matthew Caesar et al., “ROFL: Routing on Flat Labels”, ACM SIGCOMM SEP. 2006.
Mark Gritter et al., “An Architecture for Content Routing Support in the Internet”
Teemu Koponen et al., “A Data-Oriented (and Beyond) Network Architecture”, ACM SIGCOMM 07, Aug. 2007.
David R. Cheriton et al., “TRIAD: A New Next-Generation Internet Architecture”
Kevin Fall, “A Delay-Tolerant Network Architecture for challenged Internets” ACM SIGCOMM 03
Paul Francis, Ramakrishna Gummadi, “IPNL: A NAT-Extended Internet Architecture”, ACM SIGCOMM 01
Xiaowei Yang et al., “NIRA: A New Inter-Domain Routing Architecture”, IEEE/ACM Transaction on Networking 2007
Jing Su et al., “Haggle: Clean slate networking for mobile devices”, TR Cambridge University 2007
Sylvia Ratnasamy, et al., “Towards an Evolvable Internet Architecture”, ACM SIGCOMM 05
Scott Shenker et al., “Data Oriented Network Architecture: DONA”
Antonio Carzaniga et al., “A Routing Scheme for Content-Based Networking”
2016-11-27
56
ICE0602 Ubiquitous Networking
Notes: 56