## Slide 1: CS 540 Network Architecture
Lecture 3: Problems of the Internet
Prof. Younghee Lee
Some part of this teaching materials are prepared referencing the lecture note made by F. Kurose and Keith W. Ross

## Slide 2: Design Principles of Internet Protocols - Design philosophy : 40 MINS - e2e argument : 35 MINS - key advantages and problems of e2e argument : 40 MINS - rethinking and critical review of e2e argument : 35 MINS

## Slide 3: Problem of e2e principle
Inefficiency
  e.g.) End hosts do the network level functions such as retransmission, congestion control
Difficulties to implement some functions which need network level control information  SDN?
Inappropriate implementation hurt the network as well as the hosts
  Greedy sources aren’t handled well 
Weak accounting and pricing tools
Weak administration and management tools  SDN/NFV ?
Incremental deployment difficult at times
  Result of no centralized control: distributed control needed to be upgraded
    Too many systems at the same time to upgrade: No more “flag” days
    => IP ossification
  Is Software Defined Networking the solution?

## Slide 4: Rethinking the design of the Internet
Application level function can’t be built in the core of the network
  Should be implemented with the knowledge and help of the applications at the end host
But
  Operation in an untrustworthy world: attacks on end-point, spam e-mail, ..
    need more mechanism in the center of the network to enforce “good” behavior. Police in the network?
  More demanding applications: QoS?
    Installing stream servers close to the recipient?
  ISP service differentiation
  The rise of third party involvement: taxation to law enforcement, public safety, blocking of certain content
  Less sophisticated users: ease of use, cell-phone, PDA,
* David D. Clark, “rethinking the design of the Internet: The e2e arguments vs. the brave new world

## Slide 5: Rethinking the design of the Internet
Technical responses
  The different forms of e2e arguments
    Two version: 1. best effort, 2. to the design of applications, some intermediate server?
    Modify the e2e: placement of function at the edge of the network for deleting spam, pornography, eavesdrop on suspected terrorists
    Adding functions to the core of the network
      (Firewalls, traffic filters, NAT)
      Stream of data must be routed through the device
        Control element into the path of communication
      The device must have ability to see what sort of information is in the stream
        Revealing or hiding the content of messages
    Labels on information
    Trusted third parties: public-key certificates

## Slide 6: Tussle Design Principles
David D. Clark et al., “Tussle in Cyberspace: Defining Tomorrow’s Internet”, SIGCOMM’02, August 19-23
Creates competition => helps shape the tussle
The future of e2e arguments
  Innovation
    Core of network modification for new application -> high hurdle, unproven
  Reliability and robustness
    If bits of application are “in the network” => increase the number of points of failure
      Processing module for certain application services
    The more simple the core of the network, the more reliable it’s likely to be
  Evolution and enhancement of existing, mature applications is inevitable
  The most we can do to protect maturing applications is to bias the tussle
    If application designers want to preserve choice and end user empowerment,….
    we should generate “application design guidelines” that would help designers avoid pitfalls, and deal with the tussles of success.
  Keeping the net open and transparent for new applications is the most important goal
    Failures of transparency will occur -fault reporting- for tussle management (not only for tool of fault repair)

## Slide 7: Tussle Design Principles
Lesson for designer
  Failure of QoS deployment:
    ISP to deploy QoS: Why risk investment in this case?; value-transfer mechanism possibility of being rewarded
    User need to be able to exercise choice to select the ISP: competitive fear: ToS routing-through another ISP?
  Analyze the tussle: surrounding context
  Powerful force is “Tussle of competition”
    Protocol design by creating opportunities for competition => direction of evolution: How to encourage fair competition? “Disadvantages” against no innovation or no reform?
recent tussle against network neutrality
  Data service of Mobile network service provider: filtering voice traffic for Kakao talk’s voice talk

## Slide 8: Mash-up platform: Reference: Paul Golding, “Connected Services” Wiley, Sep. 2011
Left-hand side of Figure
  Telco exposing data via API
    Data related to either the users of platform or one of the key enablers of the platform such as weather forecasting venture
    Telco data: Location of customers
Right-hand side of Figure
  External innovator using the API to request and consume data from platform
  Their own business
    Not aligned with the core platform service
      Difference to previous model
  Data consumed via the APIs is mashed with the data from the application itself
  * Freemium model?: initial usage of API is free with a charge levied later on
  Examples
    Google Ads
    Amazon affiliates
Business
Provider Platform
Users
Projects
Revenue
Services
Revenue
Other innovators
Application
Other Users
Projects
Revenue
Mash-up
Services
Revenue
Low friction self serve
Mash-up platform configuration
Data
Requests

## Slide 9: Platform as a Service
Logical conclusion of platform idea
Left-hand side of Figure
  Platform: number of features that make the process of delivering services as easy and powerful as possible ???????????
Right-hand side of Figure
  Platform becomes innovators’ exclusive means of delivering service to end users
    Innovators host their applications on the platform
    Construct the applications using their own tools and processes, or using tools provided by the platform
      Use of visual programming paradigms accessible via a web browser
  Examples?
    Amazon Web Service (AWS)
      collection of remote computing services that together make up a cloud computing platform
Business
Provider Platform
Users
Projects
Revenue
Services
Revenue
Other innovators
Other Users
Platform as a service
Revenue
Services
Projects
Fee
% Revenue
In April 2015, AWS was reported to be profitable, with sales of US$1.57 billion in the first quarter of the year, and US$265 million of operating income.

## Slide 10: A critical review of e2e arguments in system design *
E2e arguments
  Firewalls, caches and NATs, active networks, multicasting and network QoS, Software Defined Networking
Ends?
  People
  File transfer applications?
  TCP?
    Applications should check integrity according to the e2e arguments.
      1. application writers do not wish to be burdened with xxx
        What about banking?
      2. error rate within the end system is negligible
    Can’t be justified on the basis of e2e arguments => trust base
* Tim Moors, “A critical review of e2e arguments in System Design”, IEEE International Conference on Communications, 2002
Application Process
Socket
TCP
Port
TCP state
communicating entity

## Slide 11: A critical review of e2e arguments in system design
Performance
  Performance benefits of localized implementation
    Error control: localized error recovery => good for latency, network load
    Multicasting: overlay multicast?
    QoS: ATM, DiffServ, IntServ, ..
  Performance benefits of e2e implementation
    Less processing required in the network
      Simple or stupid network: more scalable
    Easier to design and change
  It’s not possible to generalize the performance implications of e2e implementations
Redundancy of local implementation, network transparency, ease of deployment, decentralism

## Slide 12: A critical review of e2e arguments in system design
Mature operational commercial environment?
  E2e check is not weakly needed
  Military, R&D network case; unstable environment
Security
  “Commercial Off The Shelf(COTS) won’t divulge secret information?  link level encryption to use COTS e2e
Routing: Source routing? For what?
Congestion control
  Congestion? => network layer problem
  End point : altruistic? Selfish?
  Unnecessary performance penalty: slow start
  Hard to detect congestion at end node
  Network knows when and where adaptation is needed
Time
Congestion
Window
Initial
Slowstart
Fast
Retransmit
and Recovery
Slowstart
to pace
packets
Timeouts
may still
occur

## Slide 13: Reading Assignment
Miika Komu et. Al., “A survey of identifier–locator split addressing architectures”
Pekka Nikander, “Host Identity Protocol (HIP): Connectivity, Mobility, Multi-homing, Security, and Privacy over IPv4 and IPv6 Networks”
Submit 1 page report online via KLMS by midnight Sep. 19 which is the day before the lecture of Sep. 20 (Tue.)
Submit also 1 page report (hard copy) at the beginning of the lecture of Sep. 20 (Tue.) as attendance check and for discussion
Happy long holydays!!!