## Slide 1: CS 540 Network Architecture
Lecture 4: Mobility
Prof. Younghee Lee

## Slide 2: Mobility
Which layer can deal with mobility problem?
  Physical layer?
    limited
  Link layer?
    Campus wifi, Wibro(L2 Handover Scheme) : only limited sub-network area
  Network layer?
    Mobile IP: indirection
  Transport layer?
    End to end architecture
    TCP Migrate: dynamically re-bind endpoints => good for big, less frequent movement, no network level modifications
  Application layer?
    Web browser
    Internet Message Access Protocol(IMAP): Unlike POP, it allows multiple clients simultaneously connected to the same mailbox

## Slide 3: IP Mobility problem
IP address
  - Loc. + id
Problems of IPv4
  RIB/FIB Size
  Multi-homing
  Mobility
  IPv4 Exhaustion
A solution : Identifier/Locator split or Mobile IP
Frequent Deaggregation due to Multihoming and Mobility
* Some part of this teaching materials are prepared referencing the material presented by David Freedman – Network Manager Claranet Technology Group

## Slide 4: Discussion
Hi3: HIP + i3
SDN for redirection? or indirection?
Compatibility
Cost to build infrastructure
Your preference
How to lead to universal solution?
HIP: NAT, firewall … Can preserve their own role with HIP?

## Slide 5: MobilityFirst
MobilityFirst
  A Robust and Trustworthy Mobility-Centric Architecture for the Future Internet
  Vision: Emerging “mobile Internet” usage scenarios – pervasive/M2M/IoT Sensor Networks
* Some part of this teaching materials are prepared referencing the material presented by D. Raychaudhuri WINLAB, Rutgers University, PIMRC Keynote, Sept 13, 2011

## Slide 6: MobilityFirst : http://mobilityfirst.winlab.rutgers.edu/
(1) separation of naming and addressing, implemented via a fast global dynamic name resolution service
(2) self-certifying public key network addresses to support strong authentication and security
(3) generalized delay-tolerant routing with in-network storage for packets in transit
(4) flat-label internetwork routing with public key addresses
(5) hop-by-hop transport protocols operating over path segments rather than an end-end path
(6) a separate network management plane that provides enhanced visibility
(7) optional privacy features for user and location data
(8) an integrated computing and storage layer at routers to support programmability and evolution of enhanced network services.

## Slide 7: Conclusion
Problem of ip mobility
  Hierarchical addressing
Solution?
  flat addressing
    Arch. of flat addressing? : public key? Any other candidate?
  DNS?
Future: IoT  so many mobile node
  Things connected to Cellular network, MANET, AP….

## Slide 8: Reading Assignment
Alexander Afanasyev et al., “BGP Routing Table: Trends and Challenges”
Tian Bu et al., “On Characterizing BGP Routing Table Growth”
Submit 1 page report online via KLMS by 6pm Sep. 21 which is the day before the lecture of Sep. 22 (Thur.)
Submit also 1 page report (hard copy) at the beginning of the lecture of Sep. 22 (Thur.) as attendance check and for discussion

## Slide 9: Mobile IP Operation (FYI)
Agents advertise their presence.
  Using ICMP or mobile IP control messages
  Mobile host can solicit agent information
  Mobile host can determine where it is
Registration process: mobile host registers with home and foreign agent.
  Set up binding
Tunneling
  forward packets to foreign agent
  foreign agent forwards packets to mobile host
Supporting mobility
  invalidating old caches in a lazy fashion
Triangular problem
Source
Home
Agent
Foreign
Agent 1
Foreign
Agent 2

## Slide 10: LISP
Locator/(Endpoint)ID Separator Protocol
IETF LISP WG: RFC6830
Cisco, US
Edge-Core network separation (EID-RLOC)
  Topological Routing Locators (RLOCs) for routing
Network Based Map and Encap Solution
  encapsulation between routers at the "edge" of the Internet
  topological aggregation of the routable addresses (LOCs)
  With portable numbering of end systems (EIDs)(Separate id space)
No changes to hosts, no new addressing changes to site devices
Router:
supplies RLOCs
by adding new
header
Host Stack:
supplies IDs
Network Level Solution

## Slide 11: LISP Data plane
Ingress Tunnel Router (ITR)
Egress Tunnel Router (ETR)

## Slide 12: Mapping EID -> RLOC : Control Plane
ALT = The ALTernative network
  an instance of BGP that carries EID prefixes
ALT mapping signals ETR for ITR
  ETRs advertise EID-prefixes into the ALT to attract Map-Requests
  ITRs use the ALT to route Map-Requests to the ETRs that are authoritative for an EID prefix
  ETRs return Map-Replies on the underlying network to the requesting ITR
  The ITR can now LISP-encapsulate packets directly to the destination’s ETR: GRE
GRE: Generic Routing Encapsulation
Problem: requires global query server network
Ingress Tunnel Router (ITR)
Egress Tunnel Router (ETR)

## Slide 13: TCP connection Migration
The Migrate Internet Mobility Project:
  enabling technology for MIT’s oxygen project(Pervasive computing)
Approach
  Locates hosts through existing DNS :
    LISP: global query server network
  Secure Domain Name System Dynamic Update: RFC 2137
  Seamless connectivity through connection migration
    Follow from the e2e arguments
No IP support
  have transport layer dynamically re-bind endpoints
Join together two separate connections
  By unifying the context space: reference previous connection with token
  Initial SYN a-> : SYN/ACK <-b: ACK(with data) a-> : normal data transfer : Migrate SYN a-> : Migrate SYN/ACK <-b : ACK(with data) a->
    Special SYN packets include a Migrate option: Migrate SYNs do not establish new connections, but migrate previously-established ones
a
b

## Slide 14: Migrate approach
Slide from Alex Snoeren, MIT

## Slide 15: TCP connection Migration
The Migrate Internet Mobility Project:
  enabling technology for MIT’s oxygen project(Pervasive computing)
But
  Requires TCP support : only work for TCP
  Slower than link-layer migration

## Slide 16: HIP
The Host Identity Protocol
Invasive IP stack changes
Original goal:
  to associate secure identities with hosts via cryptography (IPSec ESP)
End-To-End Communications via HIP secure id
ID/Loc split from security perspective in addition.
HIT : Host Identity Tag
  128bit long hash value: hash on public crypto key!
  Transport sockets bound to HITs not IPs
  Kernel translates HIT - > IP
decoupling of the transport layer from the internetworking layer
Host Level Solution

## Slide 17: HIP
Process
Transport
IP layer
Link layer
Process
Transport
IP layer
Link layer
Host Identity
<IP Address, Port>
<IP Address>
<Host ID, Port>
<Host ID>
<IP Address>
New waist

## Slide 18: HIP
a signal protocol between the communicating end points
Provide implicit HI  IP mapping through FQDN  HI and FQDN  IP
IPsec ESP
The binding between host identity and IP is dynamic and can have a one-to-many relationship
Multi-homing with multiple network interface(IP address)
Security
Multi-Homing
  Ipsec: KE for e2e ESP
  + signal protocol
Mobility
Diffie-Hellman key exchange

## Slide 19: HIP
Changing address: sending a readdressing message

## Slide 20: HIP
End to End Security
Secure Mobility / Multi-homing
  IP address changes invisible to upper layers
  transport layer connections survive address changes
IPv4 / IPv6 Interworking
Connection established using a four-way handshake; the HIP base exchange
  proof of identity, IPsec setup, DoS attack protection
Kernel Support in FreeBSD, Linux, OpenSolaris, Windows

## Slide 21: Transport layer mobility
One host moves => easy:
but both of end hosts move? => NEED RECONNECTION
Good on big less frequent movement: compared to link, network level mobility

## Slide 22: ILNP
Identifier Locator Network Protocol
University of St Andrews, UK
  128bit IPv6 address -->
    64bit LOC
      names sub-networks, equivalent to an IP routing prefix,
      used by kernel to route transport binding to IP endpoint
    64bit ID
      names nodes, not interface
      TP layer uses
  a richer set of namespaces
Dynamic DNS as ID:LOC mapping system
a clean solution for the architecture?
Host Level Solution

## Slide 23: ILNPv6 Partitioning

## Slide 24: Mobility in ILNPv6
CN
  Uses DNS to find MN’s set of Identifiers and Locators
MN
  When the MN moves:
    ICMP Locator Update (LU) to inform other nodes of revised set of Locators for the MN
    Secure Dynamic DNS Update to revise its LOC in its Authoritative DNS server
Avinash Mungur, “Analysis of Locator Identity Split Protocols in Providing End-host Mobility,” Lancaster University

## Slide 25: LISP vs. HIP, ILNP
Feature | LISP | HIP | ILNP
Maturity | Production | Production (almost) | Experimental
Changes | Network | Host | Host
Site Renumber | No | Optional | Optional
Network Build | Yes | No | No
Network MTU | Increase | Retain | Retain
Reduce RIB/FIB | Yes | Yes | Yes
Mechanism | Mapping System | Inter Host | DNS
Modify Apps? | No | No | No
IPv4 | Yes | Yes | No
IPv6 | Yes | Yes | Yes
SiteMultihoming | Yes | Yes | Yes
Host Multihoming | No | No | Yes

## Slide 26: LISP vs. HIP, ILNP
Feature | LISP | HIP | ILNP
Multicast | Yes | Yes | Yes
Traffic Engineering | Yes | Yes | Yes
Local Addressing | No | No | Yes
Mobile Hosts | No | Yes | Yes
Mobile Nets | No | No | Yes
Multipathing | No | No | Yes

## Slide 27: I3: Internet Indirection Infrastructure
For mobility, multicast, anycast…
Add an indirection layer on top of IP, implemented using overlay networks
Rendezvous based
From slides of Prof. Ion Stoica, UC Berkeley
Sender
Receiver (R)
ID
R
trigger
send(ID, data)
send(R, data)
Triggers periodically refreshed by end-hosts
ID length: 256 bits
IP router
i3 node

## Slide 28: I3: Routing (DHT)
From slides of Prof. Ion Stoica, UC Berkeley
R inserts trigger t = (37, R); S sends packet p = (37, data)
An end-host needs to know only one i3 node to use i3
  E.g., S knows node 3, R knows node 35
R
3
7
20
35
41
37
R
3
7
20
35
41
37
R
S
R
trigger(37,R)
send(37, data)
send(R, data)
Chord circle
S
0
2m-1
i3 node

## Slide 29: I3: Internet Indirection Infrastructure
From slides of Prof. Ion Stoica, UC Berkeley
Sender
Receiver (R1)
p|s1
R1
send(p|a,data)
Receiver (R2)
p|s2
R2
p|s3
R3
Receiver (R3)
send(R1,data)
Sender
Receiver (R1)
id
R1
send(id,data)
send(R1, data)
Receiver (R2)
id
R2
send(R2, data)
Sender
Receiver
(R1)
id
R1
send(id,data)
send(R1, data)
Sender
Receiver
(R2)
id
R2
send(id,data)
send(R2, data)
Multicast
Mobility
Anycast
p: prefix
a: suffix
Randomly chosen suffix ? =>
Load balancing
Longest matching prefix