## Slide 1: CS 540 Network Architecture
Lecture 6: Routers
Prof. Younghee Lee
Some part of this teaching materials are prepared referencing the lecture note made by F. Kurose and Keith W. Ross

## Slide 2: Delay in packet-switched networks
packets experience delay on end-to-end path
four sources of delay at each hop
nodal processing:
  check bit errors
  determine output link
queueing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

## Slide 3: Delay in packet-switched networks
Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantitites!
http://wps.aw.com/aw_kurose_network_2/0,7240,227091-,00.html

## Slide 4: Router Architecture Overview
Two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
switching datagrams from incoming to outgoing link

## Slide 5: Input Port Functions
Decentralized switching:
given datagram dest., lookup output port using routing table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet

## Slide 6: Three types of switching fabrics

## Slide 7: Input Port Queuing
Fabric slower that input ports combined -> queueing may occur at input queues
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
queueing delay and loss due to input buffer overflow!

## Slide 8: First Generation Router (memory)
From lecture note of
Dave Andersen

## Slide 9: Second Generation Router (bus)
From lecture note of
Dave Andersen
Bottle Nexk

## Slide 10: Third Generation Router (crossbar)
From lecture note of
Dave Andersen
RIB
Control plane
Huge routing information
FIB
Data plane
Smaller
Scheduler
- input/output port to connect in a given
time slot
(If input I is connected to output j, no other input connected to j,… )
Wave front scheduler
Parallel iterative matching
iSLIP: round robin PIM
Head of Line Blocking

## Slide 11: Lookup mechanism
Exact match search:
  MPLS, ATM..
    Direct lookup
    Associative lookup: Content Addressable Memory (CAM)
      Ternary CAM: 0, 1, x x: “don’t care”
    Hashing vs. binary search
      Perfect hash function <= not easy, Update <= complex
        Multiple hash function to avoid collision
        Binary search tree
Longest Prefix match
  IP
  Not just one entry that matches a destination
    e.g., packet destination address: 143.248.56.45
      Entry 143.248.56.80/24 vs. 143.248.34.45/16 which one?
Notes: Locally connected nodes generate link-local addresses and can communicate on a shared link
Router sends Advertisement, nodes learn of global prefix and generate a global address
Site renumbering is supported by deprecation of global prefixes

## Slide 12: Longest Prefix Match: is Harder than Exact Match
The destination address of an arriving packet does not carry with it the information to determine the length of the longest matching prefix
Hence, one needs to search among the space of all prefix lengths; as well as the space of all prefixes of a given length
Metrics for Lookup Algorithms
  Speed (= number of memory accesses)
  Storage requirements (= amount of memory)
  Low update time (support ~5K updates/s)
  Scalability
    With length of prefix: IPv4 unicast (32b), Ethernet (48b), IPv4 multicast (64b), IPv6 unicast (128b)
    With size of routing table: (sweetspot for today’s designs = 1 million)
  Flexibility in implementation
  Low preprocessing time

## Slide 13: Longest Prefix Match
LPM in IPv4 Use 32 exact match algorithms for LPM!
Exact match
against prefixes
of length 1
Exact match
against prefixes
of length 2
Exact match
against prefixes
of length 32
Network Address
Port
Priority
Encode
and pick

## Slide 14: Lookup schemes
Linear search
  N: number of entries, W: Prefix length
  O(N) storage, O(N) lookup time, O(1) update complexity
  80k entries => worst case 80k lookup time? Too much long time!
Radix trie
  O(NW) storage, O(W) lookup, O(W) update complexity
PATRICIA trie
  Less storage
Caching
  Skipping LPMs
  Packet train exhibit temporal locality
  What kind of problem?
Some part of this teaching materials are prepared referencing the lecture note made by Pankaj Gupta Department of Computer Science Stanford University

## Slide 15: Tree, Tries
Trie: Prefix tree
Binary search trie: use binary tree paths to encode prefixes
Advantage: simple to implement
Disadvantage: one lookup may take O(w), where w is number of bits (32 in the case of IPv4)
001xx 2
0100x 3
10xxx 1
01100 5
0
1
0
1
0
1
1
0
0
0
0
2
3
5
1
Binary search trie
Prefix tree
<
>
<
>
<
>
>
<
<
<
Binary search tree
log2N
N entries

## Slide 16: Skip Count vs. Path Compression
Removing one way branches ensures # of trie nodes is at most twice # of prefixes; (case: trie containing a small number of very long strings)
  Patricia tries: Practical Algorithm To Retrieve Information Coded In Alphanumeric, also called as Radix trie or Radix tree: In contrast with a regular trie, the edges of a Patricia trie are labelled with sequences of characters
Using a skip count requires exact match at end and backtracking on failure  path compression simpler
P1
P2
P3
P4
0
0
0
1
1
1
1
P1
P2
P3
P4
0
0
0
1
(Skip count) Skip 2
or
11 (path compressed)
1

## Slide 17: Radix Trie
P1 | 111* | H1
P2 | 10* | H2
P3 | 1010* | H3
P4 | 10101 | H4
P2
P3
P4
P1
A
B
C
G
D
F
H
E
1
0
0
1
1
1
1
Lookup 10111
Add P5=1110*
I
0
P5
next-hop-ptr (if prefix)
left-ptr
right-ptr
Trie node
Some part of this teaching materials are prepared referencing the lecture note made by Pankaj Gupta Department of Computer Science Stanford University

## Slide 18: PATRICIA Tries
Arrange route entries into a series of bit tests
128.2/16
128.32/16
128.32.130/24
128.32.150/24
1000 0000 0000 0010 xxxx xxxx xxxx xxxx
1000 0000 0010 0000 xxxx xxxx xxxx xxxx
1000 0000 0010 0000 1000 0010 xxxx xxxx
1000 0000 0010 0000 1001 0110 xxxx xxxx
0123 4567 89. . .

## Slide 19: Multibit Tries
Binary trie
  Depth: w, Degree: 2, Stride: 1bit
Multi-bit trie
  Depth: w/k, Degree: 2k, Stride: k bits
  Reduce lookup step to almost(due to expansion) 1/k
Expanded trie
  If stride = k bits, prefix lengths that are not a multiple of k need to be expanded
  To speed up lookup, branch on multiple bits at each decision instead of just one.
  The number of bits used is the “stride length”
  Expansion uses up more space
  Also, each entry requires two fields : because some entries require both a pointer and a prefix; i.e. P2, P5, and P6
  Update speed versus memory size tradeoff
W/k

## Slide 20: Four-ary Tries (k=2)
P2
P3
P12
A
B
F
11
next-hop-ptr (if prefix)
ptr00
ptr01
A four-ary trie node
P11
10
P42
H
11
P41
10
10
11
10
D
C
E
G
ptr10
ptr11
Lookup 10111
P1 | 111* | H1
P2 | 10* | H2
P3 | 1010* | H3
P4 | 10101 | H4
A four-ary trie node
P41
Some part of this teaching materials are prepared referencing the lecture note made by Pankaj Gupta Department of Computer Science Stanford University

## Slide 21: Tree Bitmap
Used in high-speed routers : Cisco
Goal:
  Wire-speed forwarding at OC-192(10Gbps)
  Minimize memory accesses
Multibit trie
  Inside of nodes: Going back to unibit tree to avoid the problems of expansion and leaf pushing

## Slide 22: Lulea routing lookup algorithm
Three level data structure to minimize number of memory accesses and size of data structure
N = 232  4 x109

## Slide 23: Lulea routing lookup algorithm: bit vector
xx..xx01 -> not possible
Genuine head
Root head
Level2 chunks
Pointer array
Routing table

## Slide 24: Code word, bit mask and base indices
bit vector => bit mask
a(n): Number of non zero bit-masks of length 2n
  a(0) = 1 : 1
  a(1) = 12 + 1 = 2 : 11, 10
  a(2) = 22 + 1 = 5 : 1111, 1110, 1011, 1010, 1000
  a(3) = 52 + 1 = 26
  a(4) = 262 + 1 = 677 : …………………, 1000000000000000
  Number of possible bit masks: a(4) +1 = 678; 1 => 0000000000000000
16bits of ip address
First 12bits of ip address
First 10bit of ip address
bit vector
Number of bit mask: 678 < 1024 => 10 bits are enough
6 bit offset
216 = 65,536
xx..xx01 -> not possible
210 x16=
16kb

## Slide 25: Finding the pointer index
Each entry in maptable is an offset of 4 bits: Max. No. of 1’s in bit mask is less than 16
Code word array: 64kb
Base index array: 16kb
Map table: 677 x 16 x 4 : 43,4 kb
Total : 123.3 kb => 15.5 Kbyte
3 memory access

## Slide 26
33K entries: 160KB, average 2Mpps
Advantages
  Extremely small data structure – can fit in L1/L2 cache
Disadvantages
    Scalability to larger tables?
    Incremental updates not supported
Lulea routing lookup algorithm

## Slide 27: Binary Search on Prefix Intervals [Lampson98]
0000
1111
0010
0100
0110
1000
1110
1010
1100
P1
P4
P3
P5
P2
 | Prefix | Interval
P1 | /0 | 0000…1111
P2 | 00/2 | 0000…0011
P3 | 1/1 | 1000…1111
P4 | 1101/4 | 1101…1101
P5 | 001/3 | 0010…0011
1001
I1
I3
I4
I5
I6
I2
Notes: This algorithm is specific to the binary search tree data structure, that was applied to longest prefix matching by Lampson et al in 1998. To understand how the data structure is built, let us look at an example forwarding table which has 5 prefixes, each up to 4-bits long. Since the maximum length is 4-bits, each prefix can be viewed as an interval on the number line that stretches from 0 to 15. While these intervals are overlapping, the endpoints of these intervals form a set of disjoint basic intervals that cover the whole number line. There are six such basic intervals in this example.
The importance of this is that one can pre-compute the longest matching prefix for every basic interval, e.g., the LPM for interval I4 is P3. Now when a packet comes in with a destination address of say 1001, it suffices to find the basic interval that contains this point, which can be done by doing a normal binary search. In this diagram, this basic interval containing 1001 is I4 for which P3 has already been pre-computed to be the longest matching prefix.

## Slide 28
Binary Search Tree
0000
1111
0010
0100
0110
1000
1110
1010
1100
P1
P4
P3
P5
P2
I1
I3
I2
I4
I5
I6
0111
0011
1101
1100
0001

>




>
>
>
>
1001
I1
I3
I4
I5
I6
I2
 | Prefix | Interval
P1 | /0 | 0000…1111
P2 | 00/2 | 0000…0011
P3 | 1/1 | 1000…1111
P4 | 1101/4 | 1101…1101
P5 | 001/3 | 0010…0011
Notes: The binary search tree data structure for this example is shown here. The leaves contain the basic intervals while the internal nodes contain suitably chosen values to guide the search process from the root to the appropriate leaf node. For example, the lookup algorithm will traverse the path as shown for the incoming address 1001.
A binary search tree is also called an alphabetic tree because the leaves must appear in the same alphabetic order from left to right as they do lexicographically on the number line. The reason for this is simply because of the way binary search works by eliminating a chunk of “contiguous” search space with every comparison. E.g., if I3 and I6 were to be swapped, the lookup algorithm will perform a comparison with 0111 and if it takes the right branch, it assumes that it has eliminated the portion of search space to the left of 0111. But that assumption will be broken if I6 is to the left and I3 is to the right.
This is where previous work left off. We take this as our starting point and come back to our original motivation for high speed. And we make use of statistical information that routers keep anyway: that is, a count of the number of times a prefix was the LPM in recent history. That gives us a probability distribution on the access frequency of different intervals.
Lets take an example. Assume that I1 is accessed 50% of the time, I2 is accessed 25% of the time, and so on… Given this probability distribution, a natural question to ask is “what is a good alphabetic tree?”. Now Lampson’s paper does not give any suggestions? And that question is important because there are various alphabetic trees possible with the same sets of proabability values. For example this is one tree, another is …

## Slide 29: Fast Longest Prefix Match
Lulea’s Routing Lookup Algorithm (Sigcomm’97)
  use a three-level data structure
Multi-bit Tries
Controlled Prefix Expansion [Sri98]
Binary Search on Prefix Intervals [Lampson98]
Binary search on prefixes : Waldvogel – Sigcomm 97
Longest prefix matching using bloom filters – Sigcomm 2003
Route caches
  Temporal locality
  Many packets to same destination

## Slide 30: Bloom Filter
Method for representing a Set A={a1, a2,…an} of n elements (keys) to support membership queries.
Probability of a false positive
The right hand side is minimized for , in which case it becomes
Figure: A Bloom Filter with 4 hash functions.
K: number of hash functions
P1th location:
Set to 1

## Slide 31: Longest Prefix Matching using Bloom Filters
Bloom filters to find matched longest prefix
Hash Table to Next Hop
Sarang Dharmapurikar, “Longest Prefix Matching Using Bloom Filters”, Sigcomm 2003
Bloom filters can also be applied to
Service discovery,
Content discovery,
…….
Longest Prefix

## Slide 32: CAM for fast longest prefix match
Content addressable memory (CAM)
  Hardware based route lookup
  Input = tag, output = value associated with tag
  Requires exact match with tag
    Multiple cycles (1 per prefix searched) with single CAM
    Multiple CAMs (1 per prefix) searched in parallel
  Ternary CAM
    0,1,”don’t care” values in tag match
    Priority (I.e. longest prefix) by order of entries in CAM

## Slide 33: Memory Technology
Technology | Max single chip density | $/chip ($/MByte) | Access speed | Watts/chip
Networking DRAM | Very high | Cheapest | Slow | Loweat
SRAM | High | Cheap | Fast | Low
TCAM | Low | Very expensive | Fast | Very high
Notes: This is probably a good time for me to make a note. Throughout this lecture and next, you will find an almost continuous flip-flop between algorithmic analysis and real-world constraints. This is probably due to a lot of research in this field being done at the same time when industry was and is designing prcticl solutions. Hence, I think they have influenced each other heavily. That may be good or bad depending on one’s ambitions.

## Slide 34: Performance Comparison: Complexity
Algorithm | Lookup | Storage | Update
Binary trie | W | NW | W
Patricia | W2 | N | W
Path-compressed trie | W | N | W
Multi-ary trie | W/k | N*2k | -
LC trie | W | N | -
Lulea | - | - | -
Binary search on trie levels | logW | NlogW | -
Binary search on intervals | log(2N) | N | -
TCAM | 1 | N | W

## Slide 35: Performance Comparison
Algorithm | Lookup (ns) | Storage (KB)
Patricia (BSD) | 2500 | 3262
Multi-way fixed-stride optimal trie (3-levels) | 298 | 1930
Multi-way fixed-stride optimal trie (5-levels) | 428 | 660
LC trie | - | 700
Lulea | 409 | 160
Binary search on trie levels | 650 | 1600
6-way search on intervals | 490 | 950
Lookups with direct access | 15-60 | 9-33 * 1000
TCAM | 15-20 | 512

## Slide 36: Queuing Models

## Slide 37: D/D/1 Queue
  Deterministic arrivals rate 
  Deterministic service rate 
  System empty at time 0
  System unstable unless
   
  If   system stable
  E(waiting time) = 1/
  E(number in system) = /
X/Y/N
X refers to the distribution of the interarrival times
Y refers to the distribution of service times
N refers to the number of servers
G= general independent arrivals or service time
M= negative exponential distribution
D= deterministic arrivals or fixed-length service

## Slide 38: M/M/1 Queue

## Slide 39: M/M/1 Queue

## Slide 40: M/M/1 Queue(finite queue) (FYI)
Queue
=(1-Pb)
Pb


## Slide 41: M/G/1 Queue
X1
X1
X2
XM(t)
t
Residual service time r()
Time 
Poisson Arrivals See Time Averages(PASTA) property
Let Pk be the steady state probability for the queue having k customer(s).
Let Ak be the probability that the process monitor sees k customer(s) in the queue just before an arrival.
Then Pk = Ak
P(A|B) = P(AB)/P(B)
P(A|B) = P(A), when two events are independent.
Thus P(AB) = P(A)P(B)

## Slide 42: M/G/1 Queue

## Slide 43: Single-Server Queues
same message length: M/D/1
random message length: M/M/1
data entry application for a particular form
bi-modal distribution with a wide
spread between the peeks: ratio>1

## Slide 44: Self-Similar Data Traffic
A deterministic periodic function
  g(t)=g(t+aT)
  a=0,1 ,2…
nondeterministic self-similarity
  natural landscape, distribution of earthquake, ocean waves, turbulent flow, fluctuations in stock market, pattern of errors, data traffic communication channel

## Slide 45: Self-Similar Data Traffic
Continuous-time Definition(self-similar stochastic process)
  H=0.5: indicates the absence of self-similarity

## Slide 46: Examples of Self-similar Data Traffic
Ethernet Traffic
  Basic assumption is that Ethernet bandwidth is WSS
    Mean does not change with time
    Variance does on change with time
    Autocorrelation is only a function of ΔT
  actual measurement: look the same at large scale and at small scale: H  0.9
  Poisson model: each level of aggregation -> taking of a sequence of non-overlapping sample means with a sample size of 10;
    stationary ergodic stochastic process
    variance in the data to be reduced by a factor of 10 for each level of aggregation
  Self-similar model: H=0.9
  Burstiness greater when load greater
  Traditional metrics for burstiness not well-defined

## Slide 47: Examples of Self-similar Data Traffic
World wide Web Traffic
  Traffic pattern generated by the browsers -> self-similar
  On/OFF source, Pareto distribution,
  =1.16~1.5 (H=(3-)/2)
  random selection of files for transfer
    file size distribution: heavy tailed
    plenty of small files, large files(multimedia files)
Signaling System Number 7 Traffic
  SS7: the control signal protocol used on PSTN, ISDN and other digital network
  call duration: heavy tailed distribution

## Slide 48: Examples of Self-similar Data Traffic
TCP, FTP, and TELNET Traffic
  TCP: Poisson models underestimates the burstiness of TCP traffic
  TELNET:
    connection arrivals: well modeled as poisson
    packet arrivals: Poisson model underestimates the burstiness
  FTP:
    session arrivals: well modeled as poisson
    data connections: Poisson model underestimates the burstiness
    the distribution of the number of bytes in each burst: heavy upper tail
    plenty of small files, large files(multimedia files)

## Slide 49: Examples of Self-similar Data Traffic
Variable Bit Rate Video
  VBR video over ATM networks and the Internet is self-similar
  frame length: Pareto distribution
  encoded using the JPEC standard
  star wars: scene with many action, little action…-> heavy-tailed distribution of the encoded video
  long range dependence: inherent feature of VBR video traffic
Deterministic Data Transfer
  deterministic data source, varied the total load, moderately complex networks -> data traffic is self similar
  in a network with a number of protocol interactions between remote sources and destinations, the underlying protocols govern the dynamics of data traffic flow to produce self-similar behavior.

## Slide 50: Performance Implications of Self-Similarity
Ethernet/ISDN Analysis
  Poor agreement between actual waiting time and the estimated one
Ethernet data
  The higher the load on the Ethernet, the higher the estimated H or, higher degree of self-similarity
  traditional queuing models to predict performance of ATM switch node -> small buffers -> cell loss far beyond those expected -> applies to ATM, FR, 100BASE-T, WAN router, LAN, statistical Mux.

## Slide 51: Implications for Design
Loads predictable and smooth for aggregated Poisson processes, e.g., telephony, but not for networks
  More active connections means more bursty traffic
Loss/delay differ when there is long range dependence
  Linear increases in buffer size don’t help greatly
Measurement-based admission control