## Slide 1: CS 540 Network Architecture
Lecture 11 : TCP for wireless networks, MANET
Prof. Younghee Lee

## Slide 2
TCP for wireless Network
TCP assumes that packet loss is due to congestion.
Wireless Network:
  Higher transmission error rate: error prone
    Bit corruption
  Frequent handoff
  Burst error => time out => ss
  TCP assumption in wireless network( and long fat network) is not appropriate.
Problems of TCP in wireless last-hop
  Fixed + wireless link
    Delays experienced at the wired and wireless links are different: flow/congestion control
    Cellular/ wireless LAN => link delay varies with time
    Signal jamming, etc., => packet loss => RTT => …

## Slide 3
What is the problem?
Reducing cwnd make sense?
  On a CDMA channel, errors occur due to interference from other user, and due to noise
    Interference due to other users: an indication of congestion.
      interference => transmission errors => appropriate to reduce cwnd
    Noise causes errors => not appropriate to reduce cwnd.
  When a channel is in a bad state for a long duration
    It might be better to let TCP backoff, so that it does not unnecessarily attempt retransmissions while the channel remains in the bad state

## Slide 4
Proposed Solutions
e2e protocols
  Reactive: Selective ACKs (SACK), TCP-New Reno
  Proactive: TCP-Vegas, TCP-Westwood..
Split connection protocols
  Separate connections for wired path and wireless hop
  “wireless-aware TCP” (I-TCP, ProxyTCP, Snoop-TCP, split connections...)
Reliable link layer protocols
  Error correcting codes, Local retransmission

## Slide 5
Various solution
IEEE database has 599 papers on Wireless TCP

## Slide 6: TCP Vegas
Idea: source watches for some sign that some router's queue is building up and congestion will happen soon; e.g.,
  RTT is growing
  sending rate flattens
TCP Vega slow start
  ssthresh estimation via packet pair
  Only increase every other RTT
    Tests new window size before increasing
(Bottleneck Link Capacity) x Pb (or Pr or As) = (Size of a packet of packet Pair)

## Slide 7: TCP Vegas Congestion Avoidance
Only reduce cwnd if packet sent after last such action
  Reaction per congestion episode not per loss
Use change in observed end-to-end delay to detect onset of congestion
  By comparing expected to actual throughput
Other proactive congestion detection:
  (WindoeSizecurrent –WindowSizeold)x(RTTcurrent –RTTold): CARD
  When network approaches congestion -> flattening of the sending rate : Tri-S

## Slide 8: TCP Vegas
Algorithm
  let BaseRTT be the minimum of all measured RTTs (commonly the RTT of the first packet)
  if not overflowing the connection, then
    ExpectedRate = CongestionWindow / BaseRTT
  source calculates current sending rate (ActualRate)
    Actual rate = acks / round trip time; sending rate
  source compares ActualRate with ExpectedRate
    Diff = ExpectedRate - ActualRate
    if Diff < 
    -->increase CongestionWindow linearly
    else if Diff > 
    -->decrease CongestionWindow linearly
    else
    -->leave CongestionWindow unchanged
W/RTT: number of packets per sec


increase cwnd
    unchanged
decrease cwnd
cwnd is too large

## Slide 9: TCP Vegas
Fine grain timers
  Check RTO every time a dupack is received or for “partial ack”
  If RTO expired, then re-xmit packet
  Standard Reno only checks at 500ms
Allows packets to be retransmitted earlier
  Not the real source of performance gain
Allows retransmission of packet that would have timed-out
  Small windows/loss of most of window
  Real source of performance gain
  Shouldn’t comparison be against NewReno/SACK
Flaws
  Sensitivity to delay variation
  Poor performance evaluation

## Slide 10: TCP Vegas
Parameters
  : 1 packet
  : 3 packets
Example trace
Even faster retransmit
  keep fine-grained timestamps for each packet
  check for timeout on first duplicate ACK

## Slide 11: TCP Westwood (TCPW)
Sender side only modification to TCP New Reno
For better scalability and stability over high speed heterogeneous networks (including wireless)
Key idea in TCPW and ERE(Eligible Rate Estimate)
  Enhance congestion control
    Used to set cwnd after packet loss + to reset ssthresh to reach “cruising speed” fast from slow start  good for wireless network
      When three duplicate ACKs: (RE : achieved rate)
        set ssthresh RE*RTTmin : instead of ssthresh=cwnd/2 as in Reno
        If (cwnd>ssthresh) set cwnd=ssthresh
          RTTmin is set to the smallest RTT sample observed over the duration of the connection.
      When a timeout expires
        set ssthresh RE*RTTmin : instead of ssthresh=cwnd/2 as in Reno and cwnd=1
Time
Congestion
Window
Initial
Slowstart
Fast
Retransmit
and Recovery
Slowstart
to pace
packets
Timeouts
may still
occur

## Slide 12: TCP Westwood (TCPW)
ERE is estimated at the sender by sampling and exponential filtering measures from ACK stream
Samples are determined from ACK inter-arrival times and info about bytes delivered
Tk: interval
  Packet pair: reflects link capacity
  Packet train: short time throughput (aggregated data ACKed during the interval)
  No congestion => small Tk: => close to a packet pair measurement
  Congestion => larger Tk: => closer to a packet train measurement
(Bottleneck Link Capacity) x Pb (or Pr or As) = (Size of a packet of packet Pair)
dk
tk - tk-1
Expected rate with no congestion
RE: achieved rate
Severe congestion: RE =0

## Slide 13: TCP Westwood : BE
Bandwidth estimation
  ACK reception rate
  ACK conveys regarding the amount of data delivered to the destination.
  Sampled bandwidth bk at time tk (ack reception time)
  dk: the amount of the data delivered,
  Discrete-time filter which is obtained by discretizing a continuous low-pass filter using the Tustin approximation
    1/τ is the cutoff frequency of the filter

## Slide 14: TCP Westwood (TCPW)
ERE
  RE: achieved rate
    RE sampling
    REk= k* REk-1 + (1- k)*((sk+sk-1)/2):
  To obtain ERE: adapt the sample interval Tk according to congestion level
    Congestion level is similar to that in Vegas: Expected Rate - Achieved Rate
    TCPW with adaptive filter (AF)
  RE <= ERE <= BE
Expected rate with no congestion
RE: achieved rate

## Slide 15: TCP Alternatives: TCPW-A
TCPW
  after packet loss (ie, 3 DUPACKs, or Timeout), ERE is used by sender
TCPW-A: Adaptive Start
  Uses ERE to adaptively and repeatedly reset ssthresh during the startup phase
  Agile proving
  PNCD: Persistent Noncongestion Detection => agile proving to capture more bandwidth

## Slide 16: TCP Westwood (TCPW)

## Slide 17: Packet Pair in Practice(FYI)
Most Internet routers are FIFO/Drop-Tail
Easy to measure link bandwidths
  Bprobe, pathchar, pchar, nettimer, etc.
How can this be used?
  NewReno and Vegas use it to initialize ssthresh
  Prevents large overshoot of available bandwidth (by packet train)
  Want a high estimate – otherwise will take a long time in linear growth to reach desired bandwidth

## Slide 18
Wireless TCP
Reactive approach
  TCP new Reno, TCP SACK
Proactive approach
  TCP Vegas, TCP Westwood
  TCP Veno
    same methodology as Vegas
    It further suggests a way to differentiate the cause of packet loss
      If the number of backlogged packets is below a threshold
        Not congested => the loss is considered to be random.
        It increases the congestion window in a conservative manner
      Otherwise congestive => Reno scheme

## Slide 19
Wireless TCP
TCP Jersey
  the available bandwidth estimation (ABE) algorithm
    TCP sender side addition
    continuously estimates the bandwidth available to the connection
    adjust its transmission rate when the network becomes congested
  the congestion warning (CW) router configuration
    Routers alert end stations by marking all packets when there is a sign of incipient congestion.
    sender of the TCP connection
    to differentiate packet losses
  calculates the optimum congestion
  window size using ABE, CW
  ECN at the routers to implement CW

## Slide 20
Split connection approach: Indirect TCP(I-TCP)
2 TCP connections
  SACK for BS <-> MH
Advantages
  Optimize performance to wireless TCP
  No changes to TCP for FH
Disadvantages
  Violate end to end semantic: Ack..
  High overhead due to dual stack at BS, high delay due to queueing delay at BS, extra copying of data at BS
  Overhead is heavy when handoff is frequent
  BS retains hard state: BS fails? => hand-off latency increases due to state transfer…
FH
BS
BS
MH
cell2
cell1
TCP
TCP Tailored for wireless

## Slide 21
Indirect TCP(I-TCP)(2)
Implementation: proxy
I-TCP proxy
User space
Kernel
Socket layer
TCP layer
IP layer
To FH
To MH
FH socket
MH socket

## Slide 22
Indirect TCP(I-TCP)(3)
Wireless link: 2Mbps
Ethernet link: 10Mbps
Local area throughput
Wide area throughput
TCP
I-TCP
I-TCP(M->F)
TCP(F->M)
I-TCP(F->M)
TCP(M->F)

## Slide 23
Split connection approach: Variations
Selective Repeat Protocol(SRP) over UDP for tuning to wireless behavior
  Only single link: no intermediate router => reliable UDP’s are enough (?)
  Mobile-End Transport Protocol
    Terminate the TCP connection at BS
      TCP connection runs only between BS and FH
    BS pretends to be MH (MH’s IP functionality moved to BS): (metaphor: NI <-> Host)
    BS guarantees reliable ordered delivery of packets to MH
      BS-MH link can use any arbitrary protocol optimized for wireless link
  Performance better than I-TCP
    Why?
2. Asymmetric transport protocol ( Mobile-TCP)
  Lower overhead protocol at MH, higher overhead protocol at BS & FH
    Smaller header (header compression) , simpler on/off flow control, only error detection, no congestion control at wireless link ; BS does error correction
3. Mobile End Transport Protocol: BS pretends to be MH(MH’s IP function also)
FH
BS
BS
MH
cell2
cell1
TCP
SRP over UDP

## Slide 24
TCP aware link layer : snoop
UC Berkeley for wireless last-hop network: Improves on split connection
  end-to-end semantics retained
  soft state at base station, instead of hard state
Snoop agent present at BS: FH to MH
  Lost segments are detected and retransmitted locally
  Last-hop round times are estimated
  Suppression of duplicated ACKs corresponding to wireless losses avoids unnecessary invocation of fast retransmission.
    retransmit on wireless link, if packet present in buffer
  For MH to FH: Explicit Loss Notification(ELN): decoupling of retransmission from congestion control
  NACK implementation similar to TCP SACK
  Requires modification to only BS
  Not useful if TCP headers are encrypted (IPsec)
FH
BS
BS
MH
cell2
cell1
TCP
Packet retransmission

## Slide 25
WTCP
Motivation
  Snoop hides wireless losses from the sender
  But sender’s RTT estimates may be larger in presence of errors
  Larger RTO results in slower response for congestion losses
WTCP protocol
  WTCP performs local recovery, similar to Snoop
  uses the timestamp option to estimate RTT
  The base station adds base station residence time to the timestamp when processing an ack received from the wireless host
  Sender’s RTT estimate: not affected by retransmissions on wireless link

## Slide 26
Link level retransmission?
Advantages => No changes at TCP
Disadvantages
  Possible retransmission same packet at both link layer and TCP
  Reordering
  Highly variable delay
Retx on ARQ
  CDMA, TDMA use ARQ
  AIRMAIL - ARQ and FEC
  Why?
FEC?
  Correctable errors hidden from the TCP sender
  Incurs overhead => adaptive FEC [Eckhardt98]; choosing appropriate FEC dynamically
Possible choice
  Low error rate => FEC
  High / bursty error => link level retransmission

## Slide 27
Link level retransmission?
Large TCP Retransmission Timeout Intervals
  Good for reducing interference with link level retransmits
    How many times to retransmit at the link layer before giving up?
      No bound: reliable but large RTT => TCP level retransmission?
  Bad for recovery from congestion losses
  Need a timeout mechanism that responds appropriately for both types of losses: congestion loss? Link error?
When is that beneficial to TCP performance?
  in-order delivery is beneficial to TCP: selective retransmission, Go back N
  Large TCP retransmission timeout

## Slide 28
TCP for multihop wireless network
Issues in multihop wireless networks
  TCP for MANET
  Wireless Mesh Network

## Slide 29: TCP/UDP in Mobile Ad Hoc Networks
Problems of TCP in wireless ad hoc networks
  Delay incurred during a route reconstruction or reconfiguration due to the mobility of nodes in the route
  => RTT => sign of congestion => SS => performance degradation
Factors that affect TCP performance
  Wireless transmission errors
  Multi-hop routes on shared wireless medium
    For instance, adjacent hops typically cannot transmit simultaneously
    Intra-flow and inter-flow contention
  Route failures due to mobility
Data stream
ACKs stream
Two nearby flows

## Slide 30: Mobile Ad Hoc Networks
Mobility causes route changes

## Slide 31: Impact of Multi-Hop Wireless Paths [Holland99]
TCP Throughput using 2 Mbps 802.11 MAC
Connections over multiple hops are at a disadvantage compared to shorter connections, because they have to contend for wireless access at each hop

## Slide 32: Impact of Mobility: TCP Throughput- new RENO
Ideal throughput (Kbps)
measured throughput
2 m/s
10 m/s
20 m/s
30 m/s
TCPW shows much better throughput than TCP new-RENO
TCP Jersey also shows better throughput than TCP new-RENO

## Slide 33: Why Does Throughput Degrade?
mobility causes
link breakage,
resulting in route
failure
TCP data and acks
en route discarded
TCP sender times out.
Starts sending packets again
Route is
repaired
No throughput
No throughput
despite route repair
How to Improve Throughput (Bring Closer to Ideal)?
Network feedback: OK? X?
  Inform TCP of route failure by explicit message
Let TCP know when route is repaired
  Probing
  Explicit notification
Reduces repeated TCP timeouts and backoff
Why TCP fail in MANET?
  TCP misinterprets route failure or wireless error as congestion

## Slide 34: Explicit Notification: Network Feedback
Need cross layer information exchange
  Feedback (when routes break and repair)
Need modification of layer 3&4
Or provide failure notification
  ICMP “host unreachable”  TCP: suspend retransmission timer
Performance with Explicit Notification[Holland99]

## Slide 35: Performance Improvement(not enough)
Without network
feedback
2 m/s speed
With feedback

## Slide 36: Performance Improvement
Without network
feedback
With feedback
30 m/s speed
Actual throughput

## Slide 37: Why Performance Degrades With Caching
When a route is broken, route discovery returns a cached route from local cache or from a nearby node
After a time-out, TCP sender transmits a packet on the new route.
However, the cached route has also broken after it was cached
Another route discovery, and TCP time-out interval
Process repeats until a good route is found
Need mechanisms for determining when cached routes are stale
timeout due
to route failure
timeout, cached
route is broken
timeout, second cached
route also broken

## Slide 38: Approaches to TCP over Ad Hoc: TCP-F
TCP Feedback (TCP-F)
  Allows the source to be informed of a route disconnection as a result of node mobility.
  Link broken => upstream node detects => send Route Failure Notification(RFN) to the source
  The source enters SNOOZ state
    The source stops transmitting all data packets
    It freeze all timers, the current cwnd size, and value of other state variables, such as RTT estimate, RTO..
      It then initiates route failure timer: depend on the worst-case route repair time
  When route repair complete message is received
    Data transmission will be resumes and all timers and variables will be restored

## Slide 39: Approaches to TCP over Ad Hoc: TCP-BuS
Enhancement introduced
  Explicit notification
    Explicit Route Disconnection Notification(ERDN)
    Explicit Route Successful Notification(ERSN)
  Extension of timeout values:
    depend on a variety of factors : for further research
  each node can buffer ongoing packets during a route disconnection and re-establishment
  Selective retransmission
  Avoidance of unnecessary requests for fast retransmission
    Packets in transit before route disconnection ; Destination node continue to send ACK
  Reliable transmission of control message
    The source periodically sends PROBE messages to check if pivoting node receive .. or
    Each intermediate node is responsible for sending an ERSN message reliably to its upstream node until it receives data packets

## Slide 40: Approaches to TCP over Ad Hoc: ATCP
ATCP: TCP for Mobile Ad Hoc Networks [Liu 2001]
  a thin layer inserted between the standard TCP and IP layers
  explicit congestion notification (ECN) to detect congestion and distinguish congestion loss from error loss
  ICMP Destination Unreachable message to detect a change of route or temporary partition
  According to these feedbacks, the ATCP layer puts the TCP sender into either the persist, congestion control, or retransmit state accordingly
  The scheme does not modify the TCP code
  TCP semantic is maintained.

## Slide 41: ATP: A Rate-based Transport Layer Protocol
Ad-hoc Transport Protocol (ATP) [Sundaresan et. al.]
  Feedback from intermediate nodes
    path failure, queueing delay, periodic feedback on rate
  Rate based transmission
    Entirely rate-controlled. (no window concept)
    Evenly distribute transmissions over time. (reduce burstiness)
  Decoupling of congestion control and reliability
    Does not employ cumulative ACKs but solely relies on periodic SACK (with 20 SACK blocks) to identify losses.

## Slide 42
TCPs over Satellite(FYR)
Long latency, Larger congestion window or larger initial window
SACK: allow multiple packet recovery per RTT
Space Communication Protocol Standard Transport Protocol (SCPS-TP)
Satellite Transport Protocol (STP): split connection approach
Early Acks:
  Spoofing: Early acks from ground station result in faster congestion window growth
TCP-Peach [1]
  Applications such as HTTP are based on the transfer of small files
    the entire transfer occurs within the slow start phase and the connection is not able to fully utilize the available network bandwidth.
  sudden start and rapid recovery with the traditional TCP’s congestion avoidance and fast retransmit algorithms
    Sudden start introduces the use of dummy packets that are copies of the last data packet the sender has sent.
    The sender sends multiple dummy packets between two consecutive data packets
    the reception of ACKs for the dummy packets indicates the availability of the unused network resource, and the sender is triggered to increase its sending window quickly
TCP Hybla: European Satellite Network of Excellence (SatNEx) project
[1] I. F. Akyildiz, G. Morabito, and S. Palazzo, “TCP-Peach: A New Congestion Control Scheme for Satellite IP Networks,” IEEE/ACM Trans. Net., vol. 9, no. 3, June 2001, pp. 307–21.

## Slide 43
Yet another TCP variants(FYI)
Impact of mobility on TCP Performance
  Hand-off, Mobile IP
  Rendezvous Delay ; 1 sec after cell boundary crossed
  M-TCP,
  Freeze TCP
    During mobile handoff or temporary blockage of radio signals by obstacles.
    The mobile unit predicts the impending disconnections ; signal strength
    It imposes no restrictions on routers and only requires code modifications at the mobile unit or receiver side.
    The freeze-TCP receiver on the mobile unit proactively sets the advertised window size to zero in the ACK packets in the presence of impending disconnection.
      force the sender into persist mode, where it ceases sending more packets while keeping its sending window unchanged.
    To implement, cross-layer information must be exchanged,
      TCP exposed to handoff algorithms implemented by network interface card(NIC) vendors on the interface devices

## Slide 44: Discussion: picked up randomly

## Slide 45: Discussion: picked up randomly

## Slide 46: Discussion: picked up randomly
TCPW is a critical protocol in this era as wired networks are falling out of favour and wireless infrastructure have emerged which support mobility. In addition to that, it solves performance issues that have been haunting the networks due to mobility. Users no longer want to be confined to one place, they desire to be connected wherever and whenever. As future work, the benefits of link layer congestion control especially Snoop can be combined with TCPW to come up with a robust congestion detection and control mechanism.
The main issue in several papers has been that TCP assumes all packet loss is due to congestion, is there a mechanism that can help TCP learn that packet loss is not only an indicator of congestion in the network? The indicators chosen such as expected throughput are questionable, more work should be done to determine the appropriate metrics for TCP performance. Only TCP traffic was used in the simulation, it would be informative to see to TCP performance fares with other types of traffic in mobile ad hoc networks and if ELFN techniques would still be applicable. Lastly, more research should be conducted focusing on cache management improvement that would ultimately help improve TCP performance.

## Slide 47: Discussion: picked up randomly
In this paper, the main goal is regarded to prevent the false positive on the network congestion due to wireless link failure. However, isn't the further conditional check on the congestion window size drag the fast reaction on the true positive, which is the actual congestion? In the circumstance of heavy congestion, any of the status message that will be the standard of the bandwidth estimation can be indefinitely delayed. The paper criticize itself as the TCPW performs poorly when the loss rate exceeds a few percent. Hence, the further conditional check is suspected to be the reason of it, and it is wondered that this suspicion is true.
Moreover, the paper suggests the proper update of the router caches to prevent the responding with stale routers. However, it is reminded that this kind of state keeping can't be regarded as best way. If we intentionally update or reorder the cache, it is not much different with the explicit storage of the end user profiles and intermediate router profiles. If we will allow it, it is wondered why not just keep the history of the link failures in the two profiles so that we can keep track of the link failure probability.

## Slide 48: Discussion: picked up randomly
While simulation results show that TCPW flows could achieve fair shares among them, TCPW flows are not "friendly" to TCP Reno flows. However, the aggressiveness is showed1to be contained and never severe enough to lead to starvation. Future works for TCPW include comparison between TCPW and link level technique such as Snoop, further improvement of bandwidth estimation and filtering method to make TCPW more friendly, and development of control theoretical models to study about stability of TCPW.
From simulation results, we could see that TCP throughput drops greatly when node movement causes link failures, due to TCP’s inability to recognize between link failure and congestion. There are several areas for future works such as: investigation of explicit link failure notification protocol in more detail, effects of other mobile ad-hoc routing protocols have on TCP performance, and interactions between TCP and lower layer protocols when used over mobile ad-hoc networks.
Last question: Do we really need TCP over MANET? If yes, when? If no, why?