## Slide 1: CS 540 Network Architecture
Lecture 15 : SDN/NFV and P4
Prof. Younghee Lee

## Slide 2: Software Defined Networking
Separates the control plane from the data plane in network switches and routers
  Control plane: implemented in S/W in servers
  Data plane: implemented in commodity network equipment
OpenFlow: a leading SDN architecture
Which problems?
  Application: No control to networks
    No network optimization to the applications
  Hard to guarantee the QoS
  Static network management
  Too complex function and standards for 4G apps.(IMS, Parley..)
Where to use?: KT, SKT, LGU+, Daum, (NHN)…
  Cloud networking: Google announced that they achieve 100% network utilization (normally 40%)
  Mobile Network Control adaptive to dynamic app traffic behavior
    Resource virtualization, elasticity and aggregation to reduce OPEX & CAPEX
  Home networks?
  not mature to deploy for ISP
Environmental changes lead evolution: Now is time to escape from ossification?
“If header = x, send to port 4”
Flow
Table
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”
OPEX: Operational expenditures
CAPEX: Capital expenditures

## Slide 3: Open flow vs SDN
Q: What’s the difference between SDN and the OpenFlow Standard?
A:
The OpenFlow standard is a foundational element for SDN.
SDN is an emerging network architecture where network control is decoupled from forwarding and is directly programmable.
The OpenFlow Standard is the first standard communications interface defined between the control and forwarding layers of a software-defined network architecture
Open Networking Foundation (ONF)
  New non-profit standards organization (Mar 2011), Defining standards for SDN, starting with OpenFlow
https://www.opennetworking.org/

## Slide 4: OpenFlow
IP Ossification => toward
  Adoptable, self defined network rather than standard
  Programmable Network
  Give some network control to application
  with open interface
Enabling innovation on campus
Standard way to control flow-tables in commercial switches and routers
* Some part of this teaching materials are prepared referencing the material of OpenFlow Hands-on Tutorial part of the the Open Networking Summit, Stanford University Oct 17, 2011 by Mr. Brandon Heller, Papers & presentation materials of Prof. Mckeown etc.,

## Slide 5: OpenFlow: A Software Defined Networks
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
+ Competition above
 Faster innovation
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Controller 1
App
App
Controller
2
Virtualization (FlowVisor)
App
OpenFlow
Controller 1
Controller 1
Controller
2
Controller
2
Network Virtualization

## Slide 6: OpenFlow building blocks
Controller
NOX
Slicing
Software
FlowVisor
FlowVisor
Console
6
Applications
LAVI
ENVI (GUI)
Expedient
n-Casting
NetFPGA
Software
Ref. Switch
Broadcom
Ref. Switch
OpenWRT
PCEngine WiFi AP
Commercial Switches
Stanford Provided
OpenFlow
Switches
SNAC
Stanford Provided
Monitoring/ debugging tools
oflops
oftrace
openseer
OpenVSwitch
HP, NEC, Pronto, Juniper.. and many more
Beacon
Helios
Maestro
Notes: There are components at different levels that work together in making it work
The commercial switch details will follow in next slide
There are a plethora of applications possible. I only list those available at Stanford

## Slide 7: OpenFlow building blocks
OpenFlow software switch Options
  Reference Linux Switch
  NetFPGA Switch: line-rate performance for 4 Gigabit ports
  Open vSwitch: multilayer virtual switch,
OpenFlow Controller Options
  NOX: Network Operating System that supports OpenFlow switches
  Beacon: an extensible Java-based OpenFlow controller.
  Helios: an extensible C-based OpenFlow controller build by NEC
  BigSwitch: a closed-source controller based on Beacon that targets production enterprise networks
  SNAC: a controller targeting production enterprise networks based on NOX0.4
  Maestro: an extensible Java-based OpenFlow controller released by Rice Univ.

## Slide 8: OpenFlow building blocks
FlowVisor:
  a special purpose OpenFlow controller that acts as a transparent proxy between OpenFlow switches and multiple OpenFlow controllers.
  It slices the network based on the Flow fields and allocated the “flowspace” to individual controllers.
    It ensures that each controller touches only the switches and resources assigned to it.
    It partitions bandwidth and flow table resources on each switch and assigns those partitions to individual controllers.
  It enables multiple controllers to operate the same physical infrastructure
    much like a server hypervisor allows multiple operating systems to use the same x86-based hardware.
  OpenFlow controllers then operate their own individual network slices through the FlowVisor proxy.
    This allows multiple OpenFlow controllers to run virtual networks on the same physical infrastructure.

## Slide 9: OpenFlow Basics
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Flow
Table(s)
“If header = p, send to port 4”
“If header = ?, send to me”
“If header = q, overwrite header with r, add header s, and send to ports 5,6”
Rules map to packet header
Rule and Action

## Slide 10: Design Concepts
Isolation: Regular production traffic untouched
Separate intelligence (control) from the path
Virtualized and programmable: Different flows processed in different ways
Open development environment for all researchers (e.g. Linux, Verilog, etc).
Flexible definitions of a flow
  Individual application traffic
  Aggregated flows: Slice(range)
  Alternatives to IP running side-by-side => To be compatible with IP
  …

## Slide 11: Open Flow Switching
User defined processing
Data Path (Hardware)
Control Path
OpenFlow
OpenFlow Controller
OpenFlow Protocol (SSL/TCP)

## Slide 12: Flow Table Entry “Type 0” OpenFlow Switch
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + byte counters
Simple actions
Remember? Packet classification with rules & actions
Or Match

## Slide 13: Cache decisions in minimal flow-based datapath
“If header = x, send to port 4”
Flow
Table
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”

## Slide 14: Substrate: “Flowspace”
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace
“OpenFlow 2.0”

## Slide 15: Flowspace: Simple example
IP SA
IP DA
Single flow
All flows from A
A
All flows between two subnets

## Slide 16: Flowspace: Generalization
Field 2
Field 1
Single flow
Set of flows
Field n

## Slide 17: Flowspace: Maps Packets to Slices

## Slide 18: Slicing using VLANs Sliced OpenFlow Switch
Normal L2/L3 Processing
Flow Table
A VLANs
(Legacy VLANs)
Flow Table
Flow Table
C VLANs
B VLANs
Controller C
Controller B
Controller A

## Slide 19: FlowVisor
A proxy between switch and guest controller
  It slices the network based on the Flow fields and allocated the “flowspace” to individual controllers.
    Network Virtualization
Parses and rewrites OpenFlow messages as they pass
Ensures that one experiment doesn’t affect another
  Isolation
Allows rich virtual network boundaries
  By port, by IP, by flow, by time, etc.
Define virtualization rules in software
Rob Sherwood∗, Glen Gibb†, Kok-Kiong Yap†, Guido Appenzeller†, Martin Casado#, Nick McKeown†, Guru Parulkar†
∗ Deutsche Telekom Inc. R&D Lab, † Stanford University, #Nicira Networks
“FlowVisor: A Network Virtualization Layer”, OPENFLOW-TR-2009-1

## Slide 20
FlowVisor
Rob Sherwood* (rob.sherwood@stanford.edu)
OpenFlow
Switch
OpenFlow
Protocol
FlowVisor
Bob’s
Controller
Alice’s
Controller
OpenFlow
Protocol
OpenFlow
Switch
OpenFlow
Switch
* Deutsche Telekom, “T-Labs”

## Slide 21
OpenFlow Protocol
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Network Administrator’s
FlowVisor
OpenFlow Protocol
Production
Network
Controller
Alices’s
FlowVisor
GENI’s
FlowVisor
GENI
GENI
Aggregate Manager
Bob’s
FlowVisor
Learning
switch
Mobile VMs
New BGP
WiMax-WiFi
Handover
Tricast Lossless
Handover
FlowVisor

## Slide 22: NOX: A Network OS for OpenFlow

## Slide 23: Why open system? Data Center
Cost
200,000 servers
Fanout of 20 a 10,000 switches
$5k commercial switch a $50M
$1k custom-built switch a $10M
Savings in 10 data centers = $400M
Control
Optimize for features needed
Customize for services & apps
Quickly improve and innovate
Example: New data center

## Slide 24: Two Real-World Deployments
Usage control in home networks
  Implementation of user controls (e.g., usage cap management, parental controls) in home networks
  Today: Not possible
  With SDN: Intuitive, simple
Access control in enterprise networks
  Re-implementation of access control on the Georgia Tech campus network
  Today: Complicated, low-level
  With SDN: Simpler, more flexible
http://projectbismark.net/

## Slide 25: SDN use case – google inter-datacenter
Why?
  significant amount of data to be moved from one region to another
  Need Inter-Datacenter WAN with centralized Traffic Engineering(TE) using SDN and OpenFlow
Problem?
  non-linear complexity in management and configuration.”
  Source: “Migration Use Cases and Methods”, Migration Working Group, ONF 2013

## Slide 26: Open Flow: summary
www.openflow.org/wk/index.php/OpenFlow_Tutorial
Many SDN vendors, switch vendors
Can co-exist with legacy ip network

## Slide 27: OpenFlow: Discussions
How much innovative is it?
What is the magic for big success?
Are there complete OpenFlow solution for ISP?
Can it co-exist with legacy ip network?
Cost Performance???
  Additional value > Transition cost : ???
Are they in rose garden?
What will be the next step?

## Slide 28: Software Defined Networking
Vender’s equipment OS

## Slide 29: OpenFlow-enabled Transport SDN
Target multi-layer OpenFlow logical switch model: ONF

## Slide 30: OpenFlow-enabled Transport SDN
Hierarchical control architecture: ONF

## Slide 31: SDN in development
Application Domains
Data centers
Enterprise/campus
Cellular backhaul
network aware applications
application aware networks
Enterprise WiFi
WANs
Products: now much more…
Switches, routers: About 15 vendors
Software: About 6 vendors and startups

## Slide 32: Cellular industry: They claim
Recently made transition to IP
Billions of mobile users
Need to securely extract payments and hold users accountable
IP is bad at both, yet hard to change
  Why?
SDN enables industry to customize their network
  How?

## Slide 33: Network Functions Virtualization
Why?
  Shorter lifecycles of network equipment
  Need to reduce CAPEX, OPEX by flexible and agile network resources
  Need to launch timely new services: SW oriented innovation
How?
  Implementing network functions in software by IT virtualization over high capacity standard servers
rack, cable, power, cooling
network infrastructure
compute infrastructure
hypervisors
operating systems
applications
switching infrastructure
rack, cable, power, cooling
network functions
compute infrastructure
hypervisors
operating systems
applications
switching infrastructure
Hypervisor:
software layer providing the virtualization
a virtual machine monitor
“Network Functions Virtualisation”, Bob Briscoe, Chief Researcher BT 2013

## Slide 34: NFV ecosystem
Current network appliance
  Dedicated HW per site
  Hard to develop and to deploy new innovative services
  Separated Message router, CDN, DPI, Firewall, Carrier grade NAT, QoE monitor, Radio access nodes……
With NFV
  Competitive, innovative open ecosystem over High capacity servers, storages and switches
Independent
Software Vendors
Generic High Volume
Ethernet Switches
Generic High Volume Servers
Generic High Volume Storage
Orchestrated,
automatic
remote install
hypervisors

## Slide 35: Synergies btw SDN, NFV, NV
SDN: Virtualization of control/management aspect
NFV: Virtualization of (network) service aspect
Network virtualization(NV): Virtualization of network aspect
SDN + NFV
  Control network flows for optimizing NFV performance

## Slide 36: Synergies btw SDN, NFV, NV
NFV and SDN Industry Map of ONF

## Slide 37: Synergies btw SDN, NFV, NV
OpenFlow-enabled SDN benefits for NFV: ONF

## Slide 38: NFV HL Architecture and Scope - ETSI
Virtualized Network Functions (VNFs)
NFV Infrastructure (NFVI)
Physical Infrastructure
Virtual Infrastructure
Compute
Storage
Network
Virtual
Computing
Virtual
Storage
Virtual
Networking
NFV Management and
Orchestration (MANO)
VNF
VNF
VNF
VNF
NFV Scope
OSS / BSS
Service
End-Points (End-users,
Other Services)
Other Networks
Geneva, Switzerland, 4 June 2013

## Slide 39: NFV architectural model - ETSI

## Slide 40: Hypervisor
Hypervisor
  Creates Virtual CPUs, Virtual NICs, Virtual Ethernet switch
NFV Hypervisor
  Direct binding of VM to core
  Direct path btw VMs and NIC
instruction policing, mapping and emulation
Sequential thread emulation
...
Virtual
machine mgt and API
VM
VM
VM
vSwitch
NfV performance
hardware
core
core
...
core
VM
NIC
NfV Hypervisor

## Slide 41: Telco Operators: They claim
Global IP traffic growing 40-50% per year
End-customer monthly bill remains unchanged: XXX
Therefore, CAPEX and OPEX need to reduce 40-50% per Gb/s per year
But in practice, reduces by ~20% per year
SDN enables industry to reduce OPEX and CAPEX
…and to create new differentiating services
How?
Capital expenditure (CAPEX)
Operating expense (OPEX)
http://www.etnews.com/20141104000234

## Slide 42: Telco Operators: CAPEX, OPEX
“In the SDN architecture, the control and data planes are decoupled, network intelligence and state are logically centralized, and the underlying network infrastructure is abstracted from applications” ONF White Paper
New services for new revenue => short life cycle
  CAPEX should be limited.
  Software defined network can help to reduce CAPEX for new services? (Optimistic) => possible?
    Thanks to decoupling S/W development from H/W
    Open Source S/W will play key role (Antonio Manzalini, TELECOM ITALIA GROUP)
  Stateful network services with stateless IP?: skepticism
  OPEX reduction: Automatic operation

## Slide 43: A SDN Use Case
TELCO: Extremely conservative: Innovation? Short life cycle services?
SDN flexibility passes through the dynamic allocation/migration of ensembles of VMs and the associated data (e.g. configurations, rule) whilst keeping network states consistent
(Antonio Manzalini, TELECOM ITALIA GROUP)

## Slide 44: SDN Pros & Cons (Antonio Manzalini, TELECOM ITALIA GROUP)
Pros
  Decoupling H/W from S/W
    (same evolution of PC)
  Network OS: logically centralized control
  Network programmability (API)
  Opportunity of complementing with network virtualization
  Reducing time to market
  Saving Capex and Opex
Cons
  Scalability and performance ? (h/w speedup required in core nodes): States
  Consistency of network states
  (data) when logically centralizing the control ?
  Signaling overhead ?
  Availability, Complexity, Stability?
  Quite convincing for the Edge, not for the Core…

## Slide 45: What about standards
Networks need Standards that will define the interfaces
The role of standards will change:
  Network owners will define network behavior
  Features will be adopted without standards
Programming world
  Good software is adopted, not standardized
SDN(with standards) + Open sources + Cloud =>
  New ecosystem : free (service + network) platform?

## Slide 46: Virtualization
Service Virtualization
  focuses on providing a common infrastructure for building and managing a complex service ecosystem.
  an emerging trend in the SOA
  landscape
Server Virtualization
Storage Virtualization
End-to-end virtualization: Overlay
  multiple virtual networks established end-to-end over shared physical infrastructure and resources:
    multiplicity of end-user devices, computing, storage, communication networks, providers and service domains
Network Virtualization
  a method of combining the available resources in a network by splitting up the available bandwidth into channels
  Differences with Virtual Private Network?: Standard/Programmability?

## Slide 47: Good references
https://www.youtube.com/watch?v=u3zEWsole6o
  Nick McKeown ECE Colloquium: Programming the Forwarding Plane
  Very good introduction to P4, SDN and historical backgrounds
https://www.youtube.com/watch?v=fAEVYQH2BKA
  DC.p4: Programming the Forwarding Plane of a Data-Center Switch, SOSR 2015