## Slide 1: CS 540 Network Architecture
Lecture 16 : Inter-datacenter WAN
Prof. Younghee Lee

## Slide 2: Why open system? Data Center
Cost
200,000 servers
Fanout of 20 a 10,000 switches
$5k commercial switch a $50M
$1k custom-built switch a $10M
Savings in 10 data centers = $400M
Control
Optimize for features needed
Customize for services & apps
Quickly improve and innovate
Example: New data center

## Slide 3: Google Networks
Google Networking
https://atscaleconference.com/videos/lessons-learned-from-b4-googles-sdn-wan/
  Source: “Lessons Learned from B4, Google’s SDN WAN”, Subhasree Mandal July 9, 2015
  Uploaded to KLMS “google_slides_mandal.pdf”

## Slide 4: SDN use case – google inter-datacenter
Why?
  significant amount of data to be moved from one region to another
  Need Inter-Datacenter WAN with centralized Traffic Engineering(TE) using SDN and OpenFlow
Problem?
  non-linear complexity in management and configuration.”
  Source: “Migration Use Cases and Methods”, Migration Working Group, ONF 2013

## Slide 5: Google Networks
Data Center Networks
  Use merchant silicon chips
  Centralized control planes
B4:
  A software-defined WAN that supports multiple traffic classes
  Use merchant silicon chips
  Centralized control planes
B2:
  A Global WAN for user-facing traffic
  Vendor gear
  Decentralized control plane
These differences increase management complexity and pose
availability challenges
  Source: “Migration Use Cases and Methods”, Migration Working Group, ONF 2013

## Slide 6: Operational mode
Traffic
  user data copies (e.g., email, documents, audio/video files) to remote datacenters for availability/durability
  remote storage access for computation over inherently distributed data sources
  large-scale data push synchronizing state across multiple datacenters
Objective
  Leverage control at the network edge to adjudicate among competing demands during resource constraint: network load balancing
  Use multipath forwarding/tunneling to leverage available network capacity according to application priority
  Dynamically reallocate bandwidth in the face of link/switch failures or shifting application demands
run at near 100% utilization and all links to average 70% utilization over long time periods, corresponding to 2-3x efficiency improvements relative to standard practice.

## Slide 7: Architecture: B4
Traffic engineering using prioritized switch forwarding table entries on the top of baseline routing protocol: red button to fall back to shortest path routing facing critical issues
Load balancing: a custom variant of Equal Cost Multipath (ECMP) hashing
  uses a hash algorithm to choose one of the next-hop addresses among ECMP set
EBGP: external BGP runs between routers in different ASs
IBGP: internal BGP runs between routers in the same AS

## Slide 8: Why open system?: Traffic Engineering
Google’s WAN
  Internet side (user traffic)
  To/From external flows
  Manage the WAN as a system (Current Internet: node centric)
  Separate hardware from software
  Logically centralized network control
    Deadlock Resolution, Bin Packing, Scheduling/Calendaring, Predictability
LSP: Label Switched Path, a path through an MPLS network (tunnel path)

## Slide 9: SDN Applications: Google’s view
Having a centralized view allows new applications.
Many of these applications require novel research. A few of the most interesting to us are:
  Traffic Engineering
    Intra-domain
    Inter-domain egress
    optimization
    scheduling
    control theory
  Security
  Event Based Control

## Slide 10
Evolve or Die: High-Availability Design Principles
Drawn from Google’s Network Infrastructure
Slides are uploaded to KLMS “google-Evolve-Ramesh-Slides.pdf”
By learning from failures
  A small mistake by operator can impact a large part of network
From 100 Postmortem reports written over a 2 year period
  70% of failures occur when management plane operation is in progress
  Failures are everywhere: all three networks and three planes see comparable failure rates
  80% of failure durations between 10 and 100 minutes  too long
Re-think the Management Plane
  Operator types wrong CLI command, runs wrong script  Minimize Operator Intervention
  To upgrade part of a large device…  … proceed while rest of device carries traffic
  Ensure residual capacity > demand  Assess risk continuously
Avoid and Mitigate Large Failures
  Design fallback strategies  e.g.) Fallback to B2!
Make change the common case
  Make it easy and safe to evolve the network daily

## Slide 11
Evolve or Die: High-Availability Design Principles
Drawn from Google’s Network Infrastructure http://www.layer9.org/
http://www.layer9.org/2016/08/sigcomm-2016-session-2-wide-area.html
Q1) Is there an place in this work for formal methods?
A) Our paper discusses this, formal methods have not been applied at large scale networks. However, there is recent work on data plane and control plane verification and space is there for work in formal methods.
Q2) Has Google ever pressed the red button?
A) The answer is beyond my pay grade.