## Slide 1: CS 540 Network Architecture
Lecture 19 : Ad-hoc Networks, VANET
Prof. Younghee Lee

## Slide 2: Taxonomy
Wireless
Networking
Multi-hop
Infrastructure-less
(ad-hoc)
Infrastructure-based
(Hybrid)
Infrastructure-less
(MANET)
Single
Hop
Cellular
Networks
Wireless Sensor
Networks(?)
Wireless Mesh
Networks
Car-to-car
Networks
(VANETs)
Infrastructure-based
(hub&spoke)
802.11
802.16
Bluetooth
802.11

## Slide 3: Routing Protocols
Proactive protocols
  Establish routes in advance
  Traditional link-state and distance-vector routing protocols are proactive
  Table driven Routing protocol
    Destination Sequenced Distance Vector Routing(DSDV)
    Clusterhead Gateway Switch Routing(CGSR)
Reactive protocols
  Establish routes only if needed
  Less routing overhead, but higher latency in establishing the path
  Source-initiated on-demand
    AODV, DSR, LMR, TORA, ABR, SSR
Hybrid protocols
  Proactive within a restricted geographic area, reactive if a packet must traverse several of these areas
  ZRP, LANMAR

## Slide 4: Trade-Off
Latency of route discovery
  Proactive protocols: Little or no delay for route determination
    since routes are maintained at all times
  Reactive protocols: Significant delay in route determination
    Employ flooding (global search)
    Control traffic may be bursty
Overhead of route discovery/maintenance
  Proactive protocols: Consume bandwidth to keep routes up-to-date
    Maintain routes which may never be used
  Reactive protocols: Lower overhead since routes are determined on demand
Which approach achieves a better trade-off depends on the traffic and mobility patterns
  Low traffic with high mobility : Reactive : winner?
  High traffic with low mobility : Proactive

## Slide 5: Ad hoc routing protocols
Ad hoc routing protocols
Table-driven
Source-initiated
On-demand
DSDV
WRP
AODV
ABR
DSR
LMR
TORA
SSR
CGSR

## Slide 6: Proactive Protocols
Distance vector
  Finding shortest path to destination using the route information from neighbor nodes
    Bellman-ford
    Count to infinity problem
Link state
  Each node advertise link information using flooding
  Each node calculate shortest path

## Slide 7: Destination-Sequenced Distance-Vector (DSDV) [Perkins94Sigcomm]
Each node maintains a routing table which stores
  next hop towards each destination
  a cost metric for the path to each destination
  a destination sequence number that is created by the destination itself
  Sequence numbers used to avoid formation of loops : why?
Each node periodically forwards the routing table to its neighbors
  Each node increments and appends its sequence number when sending its local routing table
  This sequence number will be attached to route entries created for this node
Each route is tagged with a sequence number; routes with greater sequence numbers are preferred: newer one
When a node decides that a route is broken, it increments the sequence number of the route and advertises it with infinite metric
Node mobility : routing data update period

## Slide 8: Destination-Sequenced Distance-Vector (DSDV)
Assume that node X receives routing information from Y about a route to node Z
Let S(X) and S(Y) denote the destination sequence number for node Z as stored at node X, and as sent by node Y with its routing table to node X, respectively
Node X takes the following steps:
  If S(X) > S(Y), then X ignores the routing information received from Y
  If S(X) = S(Y), and cost of going through Y is smaller than the route known to X, then X sets Y as the next hop to Z
  If S(X) < S(Y), then X sets Y as the next hop to Z, and S(X) is updated to equal S(Y)
Avoid Count to infinity problem: how?
X
Y
Z

## Slide 9: Optimized Link State Routing (OLSR) [Jacquet00ietf]
Routers maintain awareness of current network topology by exchanging beacons(“HELLO messages”)
Each nodes tells the entire network about its immediate neighbors
Flooding the network with HELLO messages incurs too much overhead
  uses multi-point relay(MPR) nodes to decrease the number of unnecessary broadcasts (only selected nodes broadcast HELLO)

## Slide 10: Optimized Link State Routing (OLSR)
MPRs of node X are its neighbors such that each two-hop neighbor of X is a one-hop neighbor of at least one MPR of X.
  Each node transmits its neighbor list in periodic beacons, so that all nodes can know their 2-hop neighbors, in order to choose the MPR.
  The sender can select its MPRs based on the one hop node which offer the best routes to the two hop nodes.
  Upon receiving a packet, a node checks it's MPRSelector set to see if the sender has chosen the node as a MPR. If so, the packet is forwarded, else the packet is processed and discarded.
A
B
F
C
D
E
H
G
K
J
Node that has broadcast state information from A

## Slide 11: TBRPF(Topology Broadcast Based on Reverse Path Forwarding)
Full-topology link-state protocol (unlike OLSR)
Each link-state update is broadcast reliably along a dynamic min-hop-path tree rooted at the source of the update.

## Slide 12: Reactive Routing Protocols
On demand routing protocol
Large, high mobility ad hoc network
Source build routes on-demand by “flooding”
Maintain only active routes
Typically, less control overhead, better scaling properties
Drawback: route acquisition latency
DSR, AODV, LMR, TORA, ABR

## Slide 13: Dynamic Source Routing (DSR)
When node S wants to send a packet to node D, but does not know a route to D, node S initiates a route discovery
Source node S floods Route Request (RREQ)
Each node appends own identifier when forwarding RREQ
* some part of this teaching materials are prepared referencing the tutorial made by Prof. Nitin H. Vaidya University of Illinois at Urbana-Champaign

## Slide 14: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of RREQ
Z
Y
Broadcast transmission
M
N
L
[S]
[X,Y] Represents list of identifiers appended to RREQ

## Slide 15: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Node D does not forward RREQ, because node D
is the intended target of the route discovery
M
N
L
[S,E,F,J,M]

## Slide 16: Route Discovery in DSR
Destination D on receiving the first RREQ, sends a Route Reply (RREP)
RREP is sent on a route obtained by reversing the route appended to received RREQ
RREP includes the route from S to D on which RREQ was received by node D

## Slide 17: Route Reply in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
RREP [S,E,F,J,D]
Represents RREP control message

## Slide 18: Dynamic Source Routing (DSR)
Node S on receiving RREP, caches the route included in the RREP
When node S sends a data packet to D, the entire route is included in the packet header
  hence the name source routing
Intermediate nodes use the source route included in a packet to determine to whom a packet should be forwarded

## Slide 19: Data Delivery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
DATA [S,E,F,J,D]
Packet header size grows with route length

## Slide 20: Ad Hoc On-Demand Distance Vector Routing (AODV) [Perkins99Wmcsa]
DSR includes source routes in packet headers
  Resulting large headers can sometimes degrade performance
AODV attempts to improve on DSR by maintaining routing tables at the nodes, so that data packets do not have to contain routes
When a node re-broadcasts a Route Request, it sets up a reverse path pointing towards the source
  AODV assumes symmetric (bi-directional) links
When the intended destination receives a Route Request, it replies by sending a Route Reply
Route Reply travels along the reverse path set-up when Route Request is forwarded

## Slide 21: Route Reply in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Represents links on path taken by RREP
M
N
L

## Slide 22: Forward Path Setup in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
Forward links are setup when RREP travels along
the reverse path
Represents a link on the forward path
Routing table entries used to forward data packet.
Route is not included in packet header.

## Slide 23: Flooding of Control Packets
How to reduce the scope of the route request flood ?
  LAR [Ko98Mobicom]
  Query localization [Castaneda99Mobicom]
How to reduce redundant broadcasts ?
  The Broadcast Storm Problem [Ni99Mobicom]

## Slide 24: Solutions for Broadcast Storm
Probabilistic scheme: On receiving a route request for the first time, a node will re-broadcast (forward) the request with probability p
Also, re-broadcasts by different nodes should be staggered by using a collision avoidance technique (wait a random delay when channel is idle)
  this would reduce the probability that nodes B and C would forward a packet simultaneously in the previous example
Counter-Based Scheme: If node E hears more than k neighbors broadcasting a given route request, before it can itself forward it, then node E will not forward the request
  Intuition: k neighbors together have probably already forwarded the request to all of E’s neighbors

## Slide 25: Hierarchical Routing Protocols
1.CGSR (Clusterhead-Gateway Switch Routing)
2.HSR (Hierarchical State Routing)
3.ZRP (Zone Routing Protocol)
4.LANMAR (Landmark Ad Hoc Routing Protocol)

## Slide 26: Hybrid Protocols
Zone Routing Protocol (ZRP) [Haas98] combines
  Intra-zone routing: Pro-actively maintain state information for links within a short distance from any given node
    Routes to nodes within short distance are thus maintained proactively (using, say, link state or distance vector protocol)
  Inter-zone routing: Use a route discovery protocol for determining routes to far away nodes. Route discovery is similar to DSR with the exception that route requests are propagated via peripheral nodes. => Reactive

## Slide 27: Wireless Mesh Network
Wireless routers
Gateways
Printers, servers
Mobile clients
Stationary clients
Intra-mesh wireless links
Stationary client access
Mobile client access
Internet access links
Node Types
Link Types
A special type of wireless ad-hoc network

## Slide 28: Existing Routing Protocols
Internet routing protocols (e.g., OSPF, BGP, RIPv2)
  Well known and trusted
  Designed on the assumption of seldom link changes
  Without significant modifications are unsuitable for WMNs in particular or for ad hoc networks in general.
Ad-hoc routing protocols (e.g., DSR, AODV, OLSR, TBRPF)
  Newcomers by comparison with the Internet protocols
  Designed for high rates of link changes; hence perform well on WMNs
  May be further optimized to account for WMNs’ particularities
Ad Hoc
Networks
Wireless Mesh
Networks

## Slide 29: VANET

## Slide 30: VANET
Vehicular Ad hoc NETwork
  Compared to MANET
    Move at higher speeds (0-40 m/s)
    No battery and storage constraints
Opportunistic connectivity
  Like mobile sensor network
Opportunistic forwarding
  DTN

## Slide 31: VANET
Centralized V2I/I2V communications
  Wi-MAX
  Long Term Evolution (LTE)
Ad hoc V2V and centralized V2I/I2V communications
  IEEE 802.11
  IEEE 802.11p

## Slide 32: VANET
Kevin C. Lee et al., “Survey of Routing Protocols in Vehicular Ad Hoc Networks” 2012

## Slide 33: VANET
BaraaT.Sharef et al., “Vehicular communication ad hoc routing protocols: A survey” 2014

## Slide 34: VANET vs. MANET
BaraaT.Sharef et al., “Vehicular communication ad hoc routing protocols: A survey” 2014

## Slide 35: VANET

## Slide 36: VANET

## Slide 37: VANET

## Slide 38: WAVE