## Slide 1: CS 540 Network Architecture
Lecture 2: Internet Design Principles
Prof. Younghee Lee
Some part of this teaching materials are prepared referencing the lecture note made by F. Kurose and Keith W. Ross

## Slide 2: Design Principles of Internet Protocols - Design philosophy : 40 MINS - e2e argument : 35 MINS - key advantages and problems of e2e argument : 40 MINS - rethinking and critical review of e2e argument : 35 MINS

## Slide 3: Design Philosophy of Internet Protocols
Fundamental Goal
  Effective technique for multiplexed utilization of existing interconnected networks : Packet switching, Statistical mux
Second level goals
  Survivability in the face of failure: stateless, fate sharing
  Support multiple types of communication services
  Accommodate a variety of networks
  Permit distributed management of its resources
  Cost effective
  Host attachment with a low level of effort
  Be accountable
Less important

## Slide 4: Survivability
Survivability in the face of network failure?
  Communicating entities(at end nodes) should not care.
  Need to store communication state. Then where?
    Network?: Virtual Circuit?
      Need to replicated state for failure handling inside the network
        Switches need to maintain state => complicated network engineering
    Host?:
      State information at the end points
        Switches do not need to maintain state => stateless router
          =>No duplication of state information in the node of the network
        trust in host, not Network Architecture.
        => simple network engineering
        Need Fate sharing for failure handling
      Fate sharing: acceptable to lose state information associated with an entity(at end points) if (and only if), at the same time, the entity itself is lost. Especially information about transport level synchronization is stored in the host

## Slide 5: Fate Sharing
  Some state information such as number of packets sent and acknowledged must be shared between the communicating entities. If entity is lost, all state is lost with the entity.
    e.g.: OK to lose TCP state if one end point crashes
    If the low layers of the architecture lose this information, they will not be able to tell if data has been lost, and the application layer will have to cope with the loss of synchrony..
    What about 1 to n or n to n multicast? Can we extend it to all n-recipient failing?
    NAT, Firewall ???
  Virtual Circuit?
    VC switches maintain state about the communication
    Need n replicated copies for n-1 failures at switches.
    Can guarantee a particular QoS. No out-of-order problem
No state
What about Virtual circuit case?
Fate sharing
Application Process
Socket
TCP
Port
TCP state
communicating entity
Connection
State
Connection
State
Web server
Client

## Slide 6: Design goals
  Distributed management of its resources
  The Internet is now too huge network: lack of tools for distributed management ( e.g. : routing)
  Operation expenses are growing
  Small glitch at a small ISP triggers a major outage across the country : bad router information
Cost effective
  Packet header processing overhead
  End to end retransmission instead of link level retransmission?
    OK since bandwidth is becoming cheaper

## Slide 7: Design goals
  Host attachment with a low level of effort
  Narrow waist
Be accountable
  Detailed billing: Almost impossible
    Flat rate
    Complicated inter-provider payment
Security is also big problem
  Worms, viruses…
  Authentication: privacy vs. security
  Stopping spam traffic: Hard

## Slide 8: Design Philosophy of Internet Protocols
Problems
  Inefficiency
  High cost of attaching a host to the Internet
  Poor implementation or malicious implementations may hurt the network as well as host
Soft-state
  Announce state
  Refresh state
  Timeout state
  Penalty for timeout – poor performance
Flow concept
  Robust way to identify communication flows
    Possible mechanism to provide non-best effort service

## Slide 9: Stateless, fate sharing
Advantages & disadvantages of stateless network
  Good for fate sharing with entity in end host: TCP has states
    No need to inform or to be dependent to the network
  When you want some higher level of network quality of services?
  When the network load is under the 0.35?
  RESTful architecture for web services
Advantages & disadvantages of stateful network
  Network can try to provide better services over the certain path for end to end communication
  When the end node entity fails? Should the network keep the states of the path for that end node entity?
  When the network path is broken? Should network inform that? How to inform the states related to communication between the end node entity to the possible new path? Duplication in the network?
  You cannot let the other people know when you die by accident.
    No advertisement => invalidate the state

## Slide 10: End-to-End Argument
Rationale: Moving function upward in a layered system, closer to the application that uses the function
  Application requirements  the function
Think twice before implementing a functionality that you believe that is useful to an application at a lower layer
  If the application can implement a functionality correctly, implement it a lower layer only as a huge performance enhancement
J.H. Saltzer, D.P. Reed, and D.D. Clark, “End-to-End Arguments in System Design”

## Slide 11: End-to-End Argument
“end to end principle:
  The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication itself is not possible
  You should not keep state in the network?
    Right or Wrong : ???
    Soft state good, stateful bad???

## Slide 12: Example: Reliable File Transfer
Solution 1: make each step reliable, and then concatenate them
  Requires correct programs for systematic countering of threats
    Program for file transfer. What about other applications? Security? (link level, network level, e2e level)
  Acceptably small probability of each of the individual threat
    Brute force countermeasures e.g.) doing many times => uneconomical
Solution 2: end-to-end check and retry
  Multiple e2e check & retry?(instead of network level check for network problem) => some part of the system is in need of repair
  Local error control+ e2e error control vs. e2e error control.: Which one is better? Always?
OS
Appl.
OS
Appl.
Host A
Host B
OK
NE1
NE2
NE n
NE: Network Equipment

## Slide 13: Discussion
Solution 1 not complete
  What happens if the sender or/and receiver misbehave?
  The receiver has to do the check anyway!
Thus, full functionality can be entirely implemented at application layer; no need for reliability from lower layers
Is there any need to implement reliability at lower layers?
Yes, but only to improve performance
Example:
  assume a high error rate on communication network
  then, a reliable communication service at data link layer might help

## Slide 14: Trade-offs
Application has more information about the data and the semantic of the service it requires (e.g., can check only at the end of each data unit)
A lower layer has more information about constraints in data transmission (e.g., packet size, error rate)
  Note: these trade-offs are a direct result of layering!
Rule of Thumb
  Implementing a functionality at a lower level should have minimum performance impact on the application that do not use the functionality

## Slide 15: Other Examples
Secure transmission of data
  CDMA eavesdropping case in Korea

## Slide 16: Internet & End-to-End Argument
At network layer provides one simple service: best effort datagram (packet) delivery
Only one higher level service implemented at transport layer: reliable data delivery (TCP)
  performance enhancement; used by a large variety of applications (Telnet, FTP, HTTP)
  does not impact other applications (can use UDP)
Everything else implemented at application level
Why ?
  1. The complexity of the core network is reduced, which reduces costs and facilitates future upgrades to the network.
  2. Generality in the network increases the chances that a new application can be added without having to change the core of the network.
  - Specific function for specific service at core network: Good or bad ?
  3. Applications do not have to depend on the successful implementation and operation of application-specific services in the network, which may increase their reliability.

## Slide 17: Internet & End-to-End Argument
Occam’s razor
  "Entities should not be multiplied unnecessarily."
  "when you have two competing theories which make exactly the same predictions, the one that is simpler is the better.“
    "If you have two theories which both explain the observed facts then you should use the simplest until more evidence comes along"
    "The simplest explanation for some phenomenon is more likely to be accurate than more complicated explanations."
    "If you have two equally likely solutions to a problem, pick the simplest."
    "The explanation requiring the fewest assumptions is most likely to be correct."
    Many scientific researches : Newton, Einstein, Heisenberg, Steven Hawking…..
Communication subsystem is frequently specified before applications that use the subsystem are known: What I had done during around 1987 ~ 1993.: Nobody can predict the future!
    May be tempted to take on more function than necessary
    => Good examples are ATM, OSI protocols…
    E2e to reduce such temptations

## Slide 18: Key Advantages
The service can be implemented by a large variety of network technologies
Does not require routers to maintain any fined grained state about traffic. Thus, network architecture is
  Robust
  Scalable
What About Other Services?
  Multicast?
  Quality of Service (QoS)?

## Slide 19: Reading Assignment
Tim Moors, “A critical review of “End-to-end arguments in system design””
David D. Clark et al., “ Rethinking the design of the Internet: The end to end arguments vs. the brave new world ”
Submit 1 page report online via KLMS by midnight Sep. 12 which is the day before the lecture of Sep. 13 (Thur.)
Submit also 1 page report (hard copy) at the beginning of the lecture of Sep. 13 (Thur.) as attendance check and for discussion