## Slide 1: CS 540 Network Architecture
Lecture 5: Inter AS Routing
Prof. Younghee Lee

## Slide 2: BGP problem
Table growth
  Multihoming, load balancing, address fragmentation, and failure to aggregate address prefixes
Convergence
  BGP may explore many routes before finding the right new one
Correctness
  Routes may not be valid, visible, or loop-free
Instability: route flapping due to high routing update
Multiprotocol extension: IPv4, IPv6…
Security
  Hard to check veracity of information (e.g., AS path)
  Can’t tell where data traffic is actually going to go
Complex policy control: broken business model
  Universal connectivity depends on cooperation: No guarantees
BGP: simple protocol but extremely complex configuration flexibility

## Slide 3: Internet Routing Instability [Labovitz et al ’96]
Problems caused by routing instability
  Increased delays, packet loss and reordering, time for routes to converge (small-scale route changes)
Types of Inter-domain Routing Updates
  Forwarding instability: may reflect topology changes
  Policy fluctuations (Routing instability): may reflect changes in routing policy information
  Pathological updates: redundant updates that are neither routing nor forwarding instability
  Instability: forwarding instability and policy fluctuation change forwarding path

## Slide 4: BGP Information Exchange
Announcements: a router has either
  Learned of a new route, or
  Made a policy decision that it prefers a new route
Withdrawals: a router concludes that a network is no longer reachable
  Explicit: associated to the withdrawal message
  Implicit: when a route is replaced as a result of an announcement message
In steady state BGP updates should be the result only of infrequent policy changes
  Update rate  measure of network stability

## Slide 5: Routing Successive Events (Instability)
WADiff: a route is explicitly withdrawn as it becomes unreachable, and is later replaced with an alternative route (forwarding instability)
AADiff: a route is implicitly withdrawn and replaced by an alternative route as the original route becomes unavailable or a new preferred route becomes available (forwarding instability)
WADup: a route is explicitly withdrawn, and reannounced later (forwarding instability or pathological behavior)

## Slide 6: Routing Successive Events (Pathological Instability)
AADup: A route is implicitly withdrawn and replaced with a duplicate of the original route (pathological behavior or policy fluctuation)
WWDup: The repeated transmission of BGP withdrawals for a prefix that is currently unreachable (pathological behavior)

## Slide 7: Findings
BGP updates more than one order of magnitude larger than expected
Routing information dominated by pathological updates
  Implementation problems:
    Routers do not maintain the history of the announcements sent to neighbors
    When a router gets topological changes they just sent these announcements to all neighbors, irrespective of whether the router sent previous announcements about that route to a neighbor or not
  Self-synchronization – BGP routers exchange information simultaneously  may lead to link periodic link/router failures
  Unconstrained routing policies may lead to persistent route oscillations

## Slide 8: Findings
Instability and redundant updates exhibits strong correlation with load (30 seconds, 24 hours and seven days periods)
  Overloaded routers fail to respond an their neighbors withdrawn them
Instability usually exhibits high frequency
Pathological updates exhibits both high and low frequencies
No single AS dominates instability statistics
No correlation between size of AS and its impact on instability statistics
There is no small set of paths that dominate instability statistics

## Slide 9: BGP misconfiguration [Mahajan02]
How common are misconfigurations?
Their impact on connectivity and routing load?
Defined as behavior unintended by the operator
  Includes both slips (inadvertent errors) and mistakes (erroneous plan)
Two broad classes of globally visible faults
  Origin misconfiguration
  Export misconfiguration

## Slide 10: BGP misconfiguration [Mahajan02]

## Slide 11: BGP misconfiguration [Mahajan02]
Conclusions
  Misconfigurations are commonplace
  Connectivity is surprisingly robust to most misconfigs but routing load can be significant
  The causes of misconfigurations are diverse
    Much needs to be done to improve the operational reliability of the Internet

## Slide 12: Lessons: Routing
Even after decades of experience routing in the Internet is not a solved problem
This attests the difficulty and complexity of building distributed algorithm in the Internet, i.e., in a heterogeneous environment with products from various vendors
Simple protocols may increase the chance to be
  Understood
  Implemented right
  Ip, bgp protocols are supposed to be simple protocol

## Slide 13: Modeling the Process: IP address
IANA
RIR
Allocation
RIR
ISP
Allocation
ISP
BGP
Announcement
IETF
IANA
Delegation
Source: Report of Asia Pacific Network Information Center (APNIC), Paul Wilson, “IPv4 Address Lifetime”,
    Allocation of /8 blocks
    to RIRs and others
    Allocation of blocks to LIRs
  BGP routing table
Regional Internet Registries (RIRs)
Local Internet registry (LIR) or National Internet Registry (NIR)
Internet Assigned Numbers Authority

## Slide 14: IANA Allocations - Projection
Source: Report of Asia Pacific Network Information Center (APNIC), Paul Wilson, “IPv4 Address Lifetime” 2004
Prediction at 1990’: IPv4 addresses would be exhausted around 2008-2011
IANA Prediction at 2004: IPv4 addresses would be exhausted around 2020
APNIC Prediction at 2004: IPv4 addresses would be exhausted around 2027

## Slide 15: BGP Announcements - Projection
Projected date of address pool exhaustion according to BGP: 2027
Source: Report of Asia Pacific Network Information Center (APNIC), Paul Wilson, “IPv4 Address Lifetime” 2004

## Slide 16: BGP Routing Table Growth
The most obvious noise comes from flaps in /8 (Class A IP Address ) advertisements.
The first step was to remove this noise by recalculating the address data using a fixed number of /8 advertisements
  Reduce number of prefixes
Cannot discard or delete state
  … because you won’t receive the message again
Assuming exponential growth
  Address space lasts until 2025, or up to 2029
Assuming linear growth
  Address space lasts until 2037 - 2047
Source: Report of Asia Pacific Network Information Center (APNIC), Paul Wilson, “IPv4 Address Lifetime” 2004

## Slide 17: BGP Routing Table Growth
Classless Interdomain Routing (CIDR)
  Reduce number of prefixes
150,000 ~ 200,000 prefixes per RT as of 2005
  Long delay to lookup
  Table overflow
Some part of this teaching materials are prepared referencing the lecture note made by Jennifer Rexford, Princeton university

## Slide 18: BGP overload
Incremental protocol
  New route => announcement
  Withdrawal when the route is no longer available
    But no messages when nothing is changing or when RT overflow
  Cannot discard or delete state easily
    because you won’t receive the message again
Overload => all BGP session => reboot => heavy BGP load on neighbors
More prefix => more update messages => overhead, delay
BGP route flapping => unstable routing system
RIB: routing table
FIB: Smaller forwarding table for packet forwarding
  forwarding table contains only the routes which are chosen by the routing algorithm
  Often compressed to optimize for hardware storage and lookup
Network Destination | Netmask | Gateway | Interface | Metric
0.0.0.0 | 0.0.0.0 | 192.168.0.1 | 192.168.0.100 | 10
127.0.0.0 | 255.0.0.0 | 127.0.0.1 | 127.0.0.1 | 1
192.168.0.0 | 255.255.255.0 | 192.168.0.100 | 192.168.0.100 | 10
192.168.0.100 | 255.255.255.255 | 127.0.0.1 | 127.0.0.1 | 10
192.168.0.255 | 255.255.255.255 | 192.168.0.100 | 192.168.0.100 | 10

## Slide 19: CIDR
Pre-CIDR: exponential growth
With CIDR: flatter or linear growth (IETF)
With CIDR: flatter or linear growth
Steep growth: due to Internet boom and multi-homing

## Slide 20: BGP entries
Post-boom

## Slide 21: BGP Growth: Multi homing
Multi-homing is the process of selecting, provisioning, and installing a redundant connection to the Internet.
  Could be the same provider, or a different provider.
Slow is much better than dead.
  Telco circuits die., Routers die., Providers’ networks fail.
  Different networks have better performance to different sites.
All providers must advertise the prefix
Hole-punching: subnet contained in a supernet
  Detecting hole-punching
    Prefix is contained in one provider’s supernet
ISP #1
ISP #2
Stub
12.1.1.0/24
12.0.0.0/8
12.1.1.0/24
3.0.0.0/8
12.1.1.0/24
Some part of this teaching materials are prepared referencing the lecture note made by Jennifer Rexford, Princeton university
the most specific route wins
12.0.0.0/8
12.1.1.0/24
12.0.0.0/8
12.1.1.0/24

## Slide 22: BGP Growth: load balancing
Same address block is covered by several announced prefixes
  Advertise multiple subnets of a larger prefix
  Treat differently to influence incoming traffic
Detecting load balancing
  Prefixes originated by the same AS
  Could be collapsed(e.g., contiguous or contained but different attribute such as AS path)
ISP #1
ISP #2
Stub
12.1.2.0/23
12.1.2.0/24
12.1.2.0/23
12.1.3.0/24
Some part of this teaching materials are prepared referencing the lecture note made by Jennifer Rexford, Princeton university

## Slide 23: BGP Growth: Fragmentation
  Different part of the address space
    Distinct address blocks allocated to same AS
    Advertised separately in BGP
For various possible reasons (e.g., geographical dispersion), ISPs split up allocated blocks into a number of sub-blocks and announce each of these independently.
ISP #1
Stub
18.8.0.0/16
12.1.1.0/24

## Slide 24: BGP Growth: Four Causes
Address fragmentation:
  Most significant
Multi-homing
  Increasing over time
Load balancing
  Increasing over time
Failure to aggregation
  Least significant
  approximately 15 to 20% prefixes could be aggregated beyond what network operators have done
  * Transient spike due to neighbor’s BGP mistake

## Slide 25: BGP Growth: How to limit growth
Hierarchical address allocation
  Allocate smaller blocks to customers
    Reclaim address blocks when customers leave
  Hierarchical address allocation inside the ISP
Filtering Small Subnets on BGP Sessions
  Larger mask than RIR guidelines
    e.g., filter /20 and longer in 63.0.0.0/8
  Or, all prefixes with mask longer than /24
  Aggressive filtering?: risk of disconnecting some part of the Internet or thwarting load-balancing of stub ASes
Careful scoping of BGP route advertisements
Explicit minimization of FIB and RIB sizes
  RIB: Routing Information Base
    holds all routing information received from routing peers
  FIB: Forwarding Information Base
    minimum amount of information necessary to make a forwarding decision on a particular packet

## Slide 26: Reading Assignment
Nick McKeown, “Fast Switched Backplane for a Gigabit Switched Router”
Guido Appenzeller et al., “Sizing Router Buffers”
Submit 1 page report online via KLMS by 6pm Sep. 26 which is the day before the lecture of Sep. 27 (Tue.)
Submit also 1 page report (hard copy) at the beginning of the lecture of Sep. 27 (Tue.) as attendance check and for discussion

## Slide 27
BGP
Path-vector
  Record what ASes a route went through to reach the destination
    Distance vector does not give you information of the path that you will take
  Complex path selection process: path length of 2 can take more time than path length of 4 because of the inside topology of the ASes.
    Distance vector?
Some part of this teaching materials are prepared referencing the lecture note made by Hari Balakrishnan

## Slide 28
Path-Vector Protocols: BGP and IDRP
Path-vector routing
  drawback of distance-vector protocol for an exterior routing protocol
    If different routers attach different meanings to a given metric, it may not be possible to create stable, loop free-routes
    no information about AS. A AS may have different priorities from other AS.
  drawback of link-state routing protocol for an exterior routing protocol
    Different ASs may use different metrics and have different restrictions. Impossible to perform a consistent routing algorithm
    flooding across multiple ASs may be unmanageable
  provide information about which networks can be reached by a given router and the ASs that must be crossed there.
    Distance vector approach does not include a distance or cost estimate
    Each block of routing information lists all of the ASs visited to reach the destination network by this route.
  Policy routing

## Slide 29: BGP-4: Border Gateway Protocol
Assumes the Internet is an arbitrarily interconnected set of AS's.
  local traffic: traffic that originates at or terminates on nodes within an AS
  transit traffic: traffic that passes through an AS
Three types of AS’s:
  Stub AS: an AS that has only a single connection to one other AS : only local traffic
  Multihomed AS: an AS that has connections to more than one other AS, but refuses to carry transit traffic.
  Transit AS: an AS that has connections to more than one other AS, and is designed to carry both transit and local traffic.
Each AS has:
One or more border routers
One BGP speaker that advertises:
  local networks
  other reachable networks (transit AS only)
  gives path information

## Slide 30: BGP Example
Speaker for AS 2 advertises reachability to P and Q
  Network 128.96, 192.4.153, 192.4.32, and 192.4.3, can be
  reached directly from AS 2.
Speaker for backbone network then advertises
  Networks 128.96, 192.4.153, 192.4.32, and 192.4.3 can be
  reached along the path <AS 1, AS 2>.
Speaker can also cancel previously advertised paths

## Slide 31: Internet inter-AS routing: BGP
Suppose: gateway X send its path to peer gateway W
W may or may not select path offered by X
  cost, policy (don’t route via competitors AS), loop prevention reasons.
If W selects path advertised by X, then:
Path (W,Z) = w, Path (X,Z)
Note: X can control incoming traffic by controlling it route advertisements to peers:
  e.g., don’t want to route traffic to Z -> don’t advertise any routes to Z
    BGP does not mandate a policy for selecting paths

## Slide 32: Internet inter-AS routing: BGP
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 33: Why different Intra- and Inter-AS routing ?
Policy:
  Inter-AS: admin wants control over how its traffic routed, who routes through its net.
  Intra-AS: single admin, so no policy decisions needed
Scale:
  hierarchical routing saves table size, reduced update traffic
Performance:
  Intra-AS: can focus on performance
  Inter-AS: policy may dominate over performance
Problem?

## Slide 34: eBGP, iBGP
External BGP (eBGP): exchanging routes between ASes
Internal BGP (iBGP): disseminating routes to external destinations among the routers within an AS
  Most ASes have more than one “border” router that talks to other peer
  Must be loop-free, best and consistent route from each eBGP router in the AS
eBGP
iBGP

## Slide 35: Routing attribute & Route Selection
Local preference
  Numerical value assigned by routing policy: primary, backup…
AS path length
  Shortest AS path != shortest path
  AS path length hack: prepending
Shortest IGP path cost to next hop
  Hot-Potato Routing: large traffic shift?
Primary
Backup
Higher local pref
Lower local pref
Destination
D
AS 1
AS 2
AS 3
AS 4
AS Path: “1”
AS Path: “1 1”
AS Path: “3 1 1”
AS Path: “2 1”
Traffic
I
New York
Atlanta
Washington, DC
5
10
Dest.
Traffic
11
Interior Gateway Protocol (IGP): for exchanging routing information between gateways within an AS: OSPF, RIP..

## Slide 36: IDRP(Inter-Domain Routing Protocol)
Designed for IPv6
ISO standard, a superset of BGP’s functions
Key differences
  BGP operates over TCP, whereas IDRP operates over the IP used in the configuration. IDRP include its own handshaking exchange to guarantee delivery of messages: for better performance
  BGP uses 16-bit autonomous system number. IDRP uses variable-length identifiers.
  IDRP can deal with multiple internet protocols and multiple internet address scheme.
  BGP communicates a path by specifying the complete list of ASs that a path visit. IDRP is able to aggregate this information using the concept of routing domain confederation(group of ASs appear to the outside world as single AS)

## Slide 37: Policy
Goal of OSPF: figure out the best way to get from here to there
Goal of IDR: figure out the best way to get from here to there without passing through a restricted area(defines policies)

## Slide 38: Implementing Policy
Policies constrain communications: 3 different ways to implement policy
  Implementing policy with bandwidth
  Implementing policy with packet filter
  Implementing policy by restricting routing information

## Slide 39: Implementing Policy
Implementing policy with bandwidth
  allowing only limited bandwidth (0 to N bps)

## Slide 40: Implementing Policy
Implementing policy with packet filter
  constrains in the forwarding process
  most commercial routers support
  substantial computation burden on the router
  administering packet filters is a challenge: need in-depth knowledge of message formats and possible values for various fields within packets

## Slide 41: Implementing Policy
Implementing policy by restricting routing information
  policy based routing: IDRP relies on this method
  places constraints on how routers distribute routing information
  not require special calculations for every IP datagram