## Slide 1: CS 540 Network Architecture
Lecture 7: Congestion Avoidance at the Router
Prof. Younghee Lee
Some part of this teaching materials are prepared referencing the lecture note made by F. Kurose and Keith W. Ross

## Slide 2: Congestion avoidance
Motivation
  Drops are the only widely used indicator of congestion
  TCP - drops and retransmissions
    End node involvement for network congestion problem
    Why no network level involvement?(ECN, reservation? Inter-router collaboration?)
Buffer size
  Space for bursts of packets
  Latency
Load
Goodput
Kbytes/sec
Time
Congestion Avoidance
Load
Goodput
Kbytes/sec
Time
Congestion Collapse

## Slide 3: FIFO + Drop-tail Problems
Surge of congestion in TCP: slow start etc.,
  Retransmission adding to the load on the network
  Global synchronization: end hosts react to same events
Full queues
  no room for bursts of packets => problem to bursty traffic
    Remind: Buffer size => Space for bursts of packets
  Routers are forced to have large queues to maintain high utilizations => High latency ( bigger buffer -> bigger delay)
  TCP detects congestion from loss:
    Forces network to have long standing queues in steady-state
    Congestion avoidance without loss detection? Yes. How?

## Slide 4: FIFO + Drop-tail Problems
Lock-out phenomena:
  Some end hosts react to same events  Traffic gets synchronized easily  allows a few flows to monopolize the queue space:  Lock-out other flows
    Fairness problem
      Does not separate between different flows
Susceptible to misbehaving flows.
  No policing: send more packets  get more service

## Slide 5: Random Early Detection(RED)
Active Queue management
Motivation
  Surge of congestion in TCP: slow start etc.,
  Router centric congestion avoidance:
    Router does something for network layer problem
    “EPD” in TCP over ATM
  Keep the average queue size small in routers
    bigger buffer -> bigger delay
      in case of self-similar traffic (more bursts)
RED
  Proactive: packet discard before full queue (drop-tail: reactive)
  In the context of ISA, RED can be exercised on queues for elastic traffic.
    Inelastic traffic: reservation

## Slide 6: RED Design Goal
Congestion Avoidance
  detect the onset of congestion to maintain the network in a region of low delay and high throughput
Global synchronization avoidance
  implicit notification by dropping packets to as many connections as necessary
Avoidance of bias against bursty traffic
  Maintain shorter queues to accommodate bursts
Bound on average queue length
  control the average queue size and therefore average delay
Queue size should reflect ability to accept bursts rather than steady-state queuing
Fairness in drops (proportional)

## Slide 7: Design
Solution of Lock-out Problem?
  Random drop
    Packet arriving when queue is full causes some random packet to be dropped
  Drop front
    On full queue, drop packet at head of queue
  Random drop and drop front solve the lock-out problem but not the full-queues problem
Solution of Full Queues Problem?
  Drop packets before queue becomes full (early drop)
  Intuition: notify senders of incipient congestion
Avoid window synchronization
  Randomly mark packets
Avoid bias against bursty traffic: shorter queue
Some protection against ill-behaved users

## Slide 8: RED Algorithm
Calculating average queue size
  exponentially weighted average of previous queue length
    to filter out transient congestion at the router
    avg = (1-wq)avg + wqq;
    small value of weight is wq recommended: wq =0.002
      large weight value? : sensitive to transient congestion
Determining packet discard
  The closer avg is to THmax, the higher the probability of discard (*1)
  As long as avg is in the critical range
    keep a count of how many consecutive packets escape discard (*2)
    the higher the value of count, the higher the probability of discard

## Slide 9: RED Algorithm
(*1)
    (*2)

## Slide 10: RED Algorithm
Upper bound on wq depends on minth
  Want to ignore transient congestion
  Can calculate the queue average if a burst arrives
    Set wq such that certain burst size does not exceed minth Why?
Lower bound on wq to detect congestion relatively quickly. Why?
Typical wq = 0.002
minth determined by the utilization requirement
  Tradeoff between queuing delay and utilization
    Higher minth => higher utilization, longer queuing delay
Relationship between maxth and minth
  Depends on average queue increase in one RTT
  Paper suggest ratio of 2
    Current rule of thumb is factor of 3

## Slide 11: RED Algorithm
Queues aren’t full
  Bursts are accommodated
Lower latency
Smarter drops
  better feedback
  more evenly distributed

## Slide 12: Extending RED for Flow Isolation
Problem: what to do with non-cooperative flows?
Fair queuing achieves isolation using per-flow state – expensive at backbone routers
  How can we isolate unresponsive flows without per-flow state?
RED penalty box
  Monitor history for packet drops, identify flows that use disproportionate bandwidth
  Isolate and punish those flows

## Slide 13: Explicit Congestion Notification(ECN)
The goal is to provide explicit congestion notification to senders.
  Complements the implicit feedback through packet drops
Bits 6-7 of the TOS bit form the ECN field.
  The ECN-Capable Transport (ECT) bit is set by the sender to indicate that the end-points are ECN-capable
  The Congestion Experience (CE) bit is set by the router to signal congestion
The ECN is received by the receiver, who is responsible for forwarding the information to the sender.
End nodes(L4)<->network(L3): problems?
V/HL
TOS
Length
ID
Flags/Offset
TTL
Prot.
H. Checksum
Source IP address
Destination IP address
Options..

## Slide 14: Use of ECN with TCP
Receiver signals congestion to the sender by setting the ECN-Echo flag in the TCP header.
  Bit 9 in the reserved field of the TCP header
  Deals correctly with asymmetric routes
  ECN-Echo flag also used to negotiate ECN use
The TCP sender should respond to ECN feedback as if a single packet loss occurred.
  Reduce the congestion window size
ECN and RED are supposed to leverage each other.
  The router should set the CE bit if it would otherwise have dropped the packet (for a non-ECN enabled flow)
  When RED is used, this happens before the queues fill up so ECN and RED combined can result in congestion notification without packet loss

## Slide 15: Random Exponential Marking (REM)
Periodically updates a congestion measure called “price”
Price p(t)
  used to determine the marking probability
  Rate mismatch: i.e., difference between input rate and link capacity
  Queue mismatch: i.e., difference between queue length and target value
  incremented if the weighted sum of these mismatches is positive, and decremented otherwise.
  pl(t + 1) = [pl (t) + g(al(bl (t) – b*l) + xl(t) – cl(t))]+,
where g > 0 and al > are small constants. and [z]+ = max {z, 0}.
bl(t) is the aggregate buffer occupancy at queue l in period t and b*l ≥ 0 is target queue length,
xl(t) is the aggregate input rate to queue l in period t, and cl(t) is the available bandwidth to queue l in period t.
The constant a l can be set by each queue individually, and trades off utilization and queuing delay during transient.
The constant g controls the responsiveness of REM to changes in network conditions.
In equilibrium the price stabilizes, and this weighted sum must be zero.  This can hold only if the input rate equals capacity (xl = cl) and the backlog equals its target (bl = b*l )

## Slide 16: Random Exponential Marking (REM)
Marking probability
  suppose a packet traverses links l = 1, 2, …, L that have prices pl(t) in period t. Then the marking probability ml(t) at queue l in period t is
  where f > 1 is a constant.
  The end-to-end marking probability for the packet is then

## Slide 17: Random Exponential Marking (REM)
Performance of NewReno/DropTail, NewReno/RED, NewReno/REM.

## Slide 18: Random Exponential Marking (REM)
Performance of Wireless TCP
As time increases on the x-axis, the number of sources increases from 20 to 100 and the average window size decreases from 22 to 4 packets.

## Slide 19: Flow (Fair) Random Early Drop (FRED)
Review of RED
  Non-Adaptive traffic: udp based MM traffic
    Non-responsive to implicit congestion
    Danger of domination
  Adaptive(TCP) & Robust traffic
    Always has data to send: larger windows and shorter RTT values
    Non-proportional dropping among identical flows
    RED: can pick the same connection to drop packets for a short period of time
    Accepting a packet from a connection cause higher drop prob. for future packets from other connection
  Adaptive & Fragile traffic
    More sensitive to loss: smaller windows and/or longer RTT
    Bias against fragile connections
    RED: uniform loss rate regardless of the resource usage  Not guarantee fair bandwidth sharing

## Slide 20: FRED design goal
Flow Database
f2
Classifier
3
1
3
f3
f1
–
+
Strikes
Maintain a single FIFO queue but track the number of packets in the queue from each connection
Drop packets from a connection when the connection exceeds its share of the queue’s capacity
  Drops are proportional to bandwidth used
  Unresponsive flows are identified and penalized
1
fN
...
...
Network
Interface
Notes: Goals
  Extend RED
  Better Fairness
Fairness concerns here were still TCP-based; concerned about applications like Telnet (fragile, always in slowstart; constantly having to time-out because of no opportunity repeated ACKs.)
  dynamically calculated per flow thresholds based on share of queue (red-like thresholds)
  threshold equal to a multiple of the “fair share” to accommodate bursts
  strikes further restrict the share of the queue and prevent you from abusing “fair share”

## Slide 21: FRED
Maintain per flow state only for active flows (ones having packets in the buffer)
minq and maxq  min and max number of buffers a flow is allowed occupy
avgcq = average buffers per flow
Strike count of number of times flow has exceeded maxq
Non-adaptive flows
  Flows with high strike count are not allowed more than avgcq buffers
  Allows adaptive flows to occasionally burst to maxq but repeated attempts incur penalty

## Slide 22
Goal: Reduce unfairness of RED
Parameters
wq= 0.002;
minth = MIN(buffer size / 4, RTT);
maxth = 2*minth;
maxp = 0.02;
Additional parameters
avgcq: estimate for average per-flow buffer count;
maxq: maximum # of packets allowed per-flow buffer count;
minq = minimum # of packets allowed per-flow buffer count;
  2 for small buffers, 4 for large buffers;
Per-flow
qleni: number of packets buffered;
strikei: number of over-runs;
FRED design goal

## Slide 23
FRED design goal
From slides of author

## Slide 24: TCP Performance with FRED
0
10
20
30
40
50
60
70
80
90
100
0
200
400
600
800
1,000
1,200
1,400
FIFO
RED
FRED
UDP blast
TCP Throughput
(Kbytes/Sec)
Time (seconds)

## Slide 25: Discussion: picked up randomly
According to observations of proposed mechanism in this paper; how we can determine the optimum average queue size using RED gateway? It is very difficult to determine the optimum average queue size for maximizing throughput and minimizing delay. If the source rate increased then, how we can control the length of growing queue? And how we can control the rate of marked packets in network? If the number of users increases then, how we can control the queues length?
It is observed that REM has similar properties as PI controller has; it is well known that PI cannot efficiently detect the congestion. So, it is not clearly elaborated that how REM can target this issue in paper. The other few questions still need to be address: how REM can achieve fast convergence speed when providing large information? What about REM responses when dynamic traffic within networks? Finally, we need to address these shortcomings of REM algorithm.

## Slide 26: Discussion
In the paper, Fig 2 shows that conventional REM is no better than Drop tail, it seems that it conflicts with the two previous papers. What factors caused these results?
As authors wrote, this approach has a problem with its application in ECN-capability. Is this active queue management approach scalable in practice? If then, how much proportion does it takes currently?
While we could detect congestion with RED gateways, can we detect which connection(s) creates congestion. As a result, we could find out a way to reduce traffic come from this connection and give bandwidth to others?
When RED gateways detect congestion, they will either drop packets or mark congestion bit in packets’ headers. While dropping packets could help to control average queue size, is there any case that dropping packets is a bad thing to do and mark congestion bit is a better way to use?

## Slide 27: Discussion
This is enhanced by the third paper’s presented technology, FRED - that takes into account the bandwidth taken by each flow to balance both between sender nodes and by bandwidth occupied.
One advantage that the paper presents is that FRED is “more effective at isolating ill-behaved flows”. This could also be valid for voluntarily ill-behaved flows: for example, if an infected device (such as an IoT device) tries a TCP SYN flood, it will try to use as much bandwidth as possible. The usage of FRED in ISP or enterprise routers will limit the unwanted traffic.
REM: This process, however, can only be useful if end nodes behave correctly. We could imagine, for example, TCP implementations that would refuse to go back to Slow Start if they suspect that the packet loss was to force a Slow Start. The paper suggests to count every marker sent to every node, to detect incorrect behaviour. In the case of disobedience, the router could limit or block input from this node.
Studying these processes might lead us to think that these processes do not distinguish users (or flows, in the case of FRED) from each other. We might for example, as administrators, want to favor bandwidth for a particular user. In that case, we could add a system of coefficients depending on the user in the probability/price equation.

## Slide 28: Reading Assignment
Jon C.R. Bennett, “WF2Q : Worst-case Fair Weighted Fair Queueing”
Ion Stoica et al., “Core-St at eless Fair Queueing: Achieving Approximately Fair Bandwidth Allocations in High Speed Networks*”
Submit less than 1 page report online via KLMS by 6pm Oct. 3 which is the day before the lecture of Oct. 4 (Tue.)
Submit also hard copy report at the beginning of the lecture of Oct. 4 (Tue.) as attendance check and for discussion